## Slide 1: EUMETSAT NEWS
Marianne König
marianne.koenig@eumetsat.int
www.eumetsat.int

## Slide 2: 26 Member States & 5 Cooperating States *
SLOVAK REPUBLIC
AUSTRIA
BELGIUM
DENMARK
FINLAND
FRANCE
GERMANY
GREECE
IRELAND
ITALY
UNITED KINGDOM
TURKEY
SWITZERLAND
SWEDEN
SPAIN
PORTUGAL
NORWAY
NETHERLANDS
LUXEMBOURG
CROATIA
POLAND
HUNGARY
LATVIA
SLOVENIA
Member States
ROMANIA*
CZECH REPUBLIC
LITHUANIA
BULGARIA
ESTONIA
ICELAND
Cooperating States
* Pending full ratification
SERBIA
Slide: 2
MUG 2010

## Slide 3: EUMETSAT Space Segment
00
01
02
03
04
05
06
07
08
10
11
12
13
14
15
16
17
18
19
20
21
22
23
24
25
26
27
28
29
30
09
…
OCEAN SURFACE TOPOGRAPHY MISSION
JASON-2
JASON-3
JASON FOLLOW-ON
THIRD PARTY PROGRAMMES
GMES SENTINEL-3A/B
GMES SENTINEL-4
GMES SENTINEL-5
METEOSAT SECOND GENERATION
METEOSAT-8
METEOSAT-9
METEOSAT-10
METEOSAT-11
METEOSAT THIRD GENERATION
EUMETSAT POLAR SYSTEM
METOP-A
METOP-B
METOP-C
POST-EPS
METEOSAT FIRST GENERATION
METEOSAT-6
METEOSAT-7

## Slide 4: Meteosat First Generation
Operational imager mission over the Indian Ocean since 1998
3-channel radiometer (VIS, IR, WV), image repeat cycle 30 minutes

## Slide 5: Meteosat-6: An Interesting Case
Radiometric Anomaly needs correction through cross-calibration with e.g. MSG

## Slide 6: MSG – Operational Service since 2004
Meteosat-8: stand-by satellite, over 10 E, currently in "rapid scan" mode
Meteosat-9: operational satellite, over 0 deg
Some MSG facts:
12-channel radiometer ("SEVIRI")
15 minute repeat cycle for full disk scans
3 km pixel sampling distance, 1 km for HRV
Main instrument is SEVIRI (spinning enhanced visible and infrared imager)
Series of 4 MSG satellites – MSG-3 launch in 2012, MSG-4 in 2014

## Slide 7: SEVIRI Overview
1
2
3
12
4
5
6
7
8
9
10
11

## Slide 8: HRV: A Special Case
High data rate allows only transmission of half a scan line. Two blocks of "half lines" can be selected.
(current setup)

## Slide 9: HRV Coregistration with other Channels
Full disk:
3712 Lines
3712 Elements per line
HRV:
3712 * 3 = 11136 Lines
(3712 * 3) / 2 = 5568 Elements

## Slide 10: HRV Coregistration with other Channels
Full disk:
3712 Lines
3712 Elements per line
HRV:
3712 * 3 = 11136 Lines
(3712 * 3) / 2 = 5568 Elements
But:
Alignment of the two grids:
SE Image Corner
HRV 1 km
Other 3km channels,
“intuitive”
First pixel in first row in SE corner:
Center of HRV Pixel (1,1) coincides with center of 3km-Pixel (1,1)
Other 3km channels,
“true”

## Slide 11: HRV Coregistration with other Channels
Full disk:
3712 Lines
3712 Elements per line
HRV:
3712 * 3 = 11136 Lines
(3712 * 3) / 2 = 5568 Elements
NW Corner – McIdas (1,1):
HRV 1 km
Other 3km channels,
“intuitive”
For the NW corner (mcidas (1,1) ):
First 3km-Pixel coincides with HRV Pixel (3,3)
Other 3km channels,
“true”

## Slide 12: Meteosat-8: Rapid Scanning Service
Repeat Cycle 5 min
Position 9.5 E
HRV window in orange

## Slide 13: MSG Benefits
Long list of NWP and Nowcasting applications
Hot topic in 2010: Volcanic Ash from Eyjafjalla eruption

## Slide 14: MSG Calibration: GSICS
One GSICS Product:
Daily cross-calibration to IASI
http://www.eumetsat.int/Home/Main/AboutEUMETSAT/InternationalRelations/CGMS/SP_1226312587804

## Slide 15: European Polar System EPS
Metop-A is Europe’s first operational polar orbiting weather satellite, in orbit since 2006. Metop-B will be launched on 02 April 2012.
09:30 ECT descending node
Suite of instruments for imaging and sounding capabilities, active radar:
AVHRR, AMSU, MHS, IASI, GOME, GRAS, ASCAT

## Slide 16: AVHRR on Metop: Global 1km Resolution

## Slide 17: Polar Winds from AVHRR

## Slide 18: GOME: Sensitivity Loss since Launch
Wavelength: 240 – 780 nm in ~4000 channels
Time since Launch
40 – 100% Throughput

## Slide 19: GRAS – Radiooccultation Instrument
Ongoing:
Update of processing software to wave optics:
Wave Optics open possibility to retrieve profiles down to ~2 km height

## Slide 20: IASI: CO Retrievals – Russian Fires in 2010

## Slide 21: Metop HRPT Zones

## Slide 22: Metop-B: 48 min Separation to Metop-A

## Slide 23: JASON-2: EUMETSAT – NASA – NOAA - CNES
Launched in 2008
Main payload: ocean surface altimeter
To be continued through JASON-3 (2011-2013) and Sentinel-3 beyond 2013
Water gauge measurements
Satellite radar

## Slide 24: Future: Meteosat Third Generation
Twin Satellite Configuration, 3-axis stabilised platforms:
MTG-I: Imager Satellite carrying the FCI instrument (Flexible Combined Imager), the Lighning Imager (LI) and the Data Collection and SAR packages
MTG-S: Sounder Satellite carrying the hyper-spectral infrared sounder IRS and a UVN instrument for GMES (Sentinel-4)
Final operational configuration:
2 imaging satellites for full disk and regional scans
1 sounder satellite
Full programme: 4 MTG-I and 2 MTG-S satellites

## Slide 25: MTG-I: Imager
Coverage Repeat cycle Full Disk Coverage 18ox18o 10 min
Local Area Cov. 1/4 FD 10/4 min
Launch of first MTG-I anticipated for 2016,
second MTG-I in ~2022
(I3 in 2025, I4 in 2029)
16 channels, spatial resolution between 0.5 and 2 km

## Slide 26: MTG-I Lightning Instrument
LIS - December
LIS - June
Provision of continuous lightning information (IC + GC) from the 0deg position

## Slide 27: MTG-S
IRS: 700-1210 cm-1,
and 1600-2175 cm-1 @0.625 cm-1 resolution
Spatial resolution at nadir: 4km

## Slide 28: MTG-S UVN Sounder
The GMES Sentinel-4 (S4) sounding mission is achieved through the Ultraviolet, Visible & Near-infrared (UVN) Instrument accommodated on the MTG-S satellites
  covering Europe every hour
  taking measurements in three spectral bands (UV: 305 - 400 nm; VIS: 400 - 500 nm, NIR: 750 - 775 nm)
  with a resolution around 8km.
The primary data products are O3, NO2, SO2, HCHO and aerosol optical depth.

## Slide 29: Very much Future: Post-EPS or EPS-SG
JPS Notional Assignments |  | Orbit, Operator, Satellites, Instruments |  | 
 |  | 05:30 (LTDN) | 09:30 (LTDN) | 13:30 (LTAN)
 |  | DoD | EUMETSAT | NOAA
Instrument Type | Provider | DWSS | EPS-SG Satellites | JPSS-1/2/3+
Visible/Infrared Imager | NOAA | VIIRS(TBC) |  | VIIRS
 | EUMETSAT |  | METimage | 
Low Light Imager | NOAA |  | LLI | 
Infrared Sounder | NOAA |  |  | JPSS-1/2: CrIS
 | EUMETSAT |  | IASI-NG | JPSS-3+: IASI-NG
Microwave Sounder | NOAA | MW Sensor | ATMS | ATMS
 | EUMETSAT |  | MWS (option) | 
Microwave Imager | NOAA | MW Sensor |  | GCOM AMSR-2 Data
 | EUMETSAT |  | MWI (Cloud/Precipitation) | 
Scatterometer | NOAA | Possibly in dedicated constellation |  | 
 | EUMETSAT |  | SCA | 
Atmospheric Chemistry | EUMETSAT |  | GMES Sentinel-5 | 
 | NOAA |  |  | OMPS N&L
Aerosol | EUMETSAT |  | 3MI | 
 | NOAA |  |  | 
Radio Occultation | NOAA | Pursuing dedicated constellation (COSMIC f/o) |  | 
 | EUMETSAT |  | RO | 
Space Environment | NOAA | SEM-N(TBC) | SEM-N(TBC) | SEM-N(TBC)
Earth Radiation | NOAA |  | CERES f/o | CERES f/o
Solar Irradiance | NOAA |  |  | TSIS (may be on a small sat)
Data Collection | NOAA |  |  | ARGOS-4 (may be on a small sat)
 | EUMETSAT |  | ARGOS-4 | 
Search and Rescue | NOAA |  | S&R | S&R (may be on a small sat)
EPS-SG is part of Joint Polar System with US
Phase-A studies will start in 2010/2011
Concept studies for METimage and IASI-NG in progress
Launch need >2020, possibly multi-satellite constellation

## Slide 30: Bright Future for Weather Satellites
And they are bright on the sky:
Metop-A Flare: photographed on 18 Sept 2010 in Darmstadt, 10sec shutter speed
flare = sunlight reflection on ASCAT antenna
Photo copyright Dieter Klaes