## Slide 1: The Challenge of VIIRS Imagery in McIDAS-X: How McIDAS Experience Helps
Don Hillger
Don.Hillger@noaa.gov
StAR Lead
VIIRS EDR Imagery and Visualization Team
NOAA/NESDIS/StAR/RAMMB
Fort Collins CO
MUG Meeting, Madison WI, 9-12 September 2013

## Slide 2: VIIRS Bands and Bandwidths
VIIRS Band | Central Wavelength (μm) | Bandwidth (μm) | Wavelength Range (μm) | Band Explanation | Spatial Resolution (m) @ nadir
M1 | 0.412 | 0.02 | 0.402 - 0.422 | Visible / Reflective | 750 m
M2 | 0.445 | 0.018 | 0.436 - 0.454 |  | 
M3 | 0.488 | 0.02 | 0.478 - 0.488 |  | 
M4 | 0.555 | 0.02 | 0.545 - 0.565 |  | 
M5 (B) | 0.672 | 0.02 | 0.662 - 0.682 |  | 
M6 | 0.746 | 0.015 | 0.739 - 0.754 | Near IR | 
M7 (G) | 0.865 | 0.039 | 0.846 - 0.885 |  | 
M8 | 1.240 | 0.020 | 1.23 - 1.25 | Shortwave IR | 
M9 | 1.378 | 0.015 | 1.371 - 1.386 |  | 
M10 (R) | 1.61 | 0.06 | 1.58 - 1.64 |  | 
M11 | 2.25 | 0.05 | 2.23 - 2.28 |  | 
M12 | 3.7 | 0.18 | 3.61 - 3.79 | Medium-wave IR | 
M13 | 4.05 | 0.155 | 3.97 - 4.13 |  | 
M14 | 8.55 | 0.3 | 8.4 - 8.7 | Longwave IR | 
M15 | 10.763 | 1.0 | 10.26 - 11.26 |  | 
M16 | 12.013 | 0.95 | 11.54 - 12.49 |  | 
DNB | 0.4 | 0.5 - 0.9 | Visible | Visible / Reflective | 750 m across full scan
I1 (B) | 0.64 | 0.08 | 0.6 - 0.68 | Visible / Reflective | 375 m
I2 (G) | 0.865 | 0.039 | 0.85 - 0.88 | Near IR | 
I3 (R) | 1.61 | 0.06 | 1.58 - 1.64 | Shortwave IR | 
I4 | 3.74 | 0.38 | 3.55 - 3.93 | Medium-wave IR | 
I5 | 11.45 | 1.9 | 10.5 - 12.4 | Longwave IR | 
Notes:
M-bands highlighted in pale yellow are available as EDRs, in addition to SDRs.
True-color component bands are highlighted in red, green, and blue.
Natural-color component bands are noted with R, G, and B.

## Slide 3: NPP/JPSS data sources
GRAVITE1 (Suitland, 7-hour delay)
NOAA CLASS2 (Asheville, 7-hour delay) – not actively used
Atmosphere PEATE3 (Wisconsin, 7-hour delay)
  ADDE server for McIDAS-X
  FTP and HTML
Direct Readout (Wisconsin, minimal delay, but provides data only over North America, when the satellite is with sight of Madison)
AFWA IDPS4 (Omaha, near real-time)
1Government Resource for Algorithm Verification, Independent Test, and Evaluation
2Comprehensive Large Array-data Stewardship System
3Product Evaluation and Algorithm Test Elements
4Air Force Weather Agency Interface Data Processing Segment

## Slide 4: Suomi NPP Imagery and Visualization Team web page http://rammb.cira.colostate.edu/projects/npp/

## Slide 5: Suomi NPP VIIRS Online http://rammb.cira.colostate.edu/ramsdis/online/npp_viirs.asp

## Slide 6: JPSS/Suomi NPP VIIRS Imagery Blog
http://rammb.cira.colostate.edu/projects/npp/blog/
Blog maintained at CIRA to highlight capabilities of VIIRS instrument.
Designed to provide education/outreach of VIIRS imagery applications.
Blog covers wide range of topics: tropical cyclones, severe weather, fire detection, auroras, volcanic eruptions, flooding, snow and ice detection, DNB applications, RGB composites and other interesting high-resolution imagery from VIIRS

## Slide 7: Beginner’s Guide to VIIRS Imagery Data
Curtis Seaman
CIRA/Colorado State University
http://rammb.cira.colostate.edu/projects/npp/Beginner_Guide_to_VIIRS_Imagery_Data.pdf

## Slide 8
VIIRS | Lines x Elements | Suggested McIDAS-X magnification
Size (km) | ~550 km x ~3000 km (~5° x ~27°) | 
I-bands (full size) | 1536 x 6400 | -2 x -4
M-bands (full size) | 768 x 3200** | 1 x -2
Suggested McIDAS-X window | 768 x 1600*** or 768 x 1920 | 1 x 1 (with LINE=X 800) to get center half of granule 1 x 1 (with LINE=X 640) to get center of granule between outermost bowtie deletions
DNB (full size) | 768 x 4064 | 
Suggested McIDAS-X window | 768 x 2032 or 786 x 1600 (same size as other bands) | 1 x 1 (with LINE=X 1016) to get center half of granule 1 x 1 (with LINE=X 1232) to get center portion of granule same size as other bands
NCC (from DNB) | 768 x 3200** | [Same treatment as M-bands]
Each granule, ~86 seconds long, or ~556 km along track
*Based on an altitude of 833 km
**48 scans x 16 detectors/scan = 768 lines
***Based on a McIDAS window as large as most single monitors will display
VIIRS single granule information

## Slide 9: VIIRS granule display in McIDAS-X (band M5 example)
Full 90-second granule (768 x 3200)
(Bow-tie deletions at each end of SDR granule are filled)
Center half of granule (768 x 1600)
(Avoids filled-in bow-tie deletion areas at each end of SDR granule)
Notes: Granules provided by Atmos PEATE via an ADDE server. Example is a M5 (visible/red band) SDR with bow-tie deletions (at ends of the granule) filled in.
(SDR = Sensor Data Record. Each granule is only ~90 seconds of VIIRS)

## Slide 10: Full 90-second granule remapped to Mollweide projection (in McIDAS-X)

## Slide 11: 16 M-band detectors per scan (red pixels are bowtie deletion pixels, first one then two lines.) Should be a repeating pattern every 16 lines.
Right half
Left half

## Slide 12
Sequential lines missing (M-bands) | 2 | 1 | 0 | 1 | 2
Lines missing out of 16 lines/scan (M-bands) | 4 | 2 | 0 | 2 | 4
Elements (M-bands) | 1-640 | 641-1008 | 1009-2192 | 2193-2560 | 2561-3200
Number of elements (M-bands) | 640 | 368 | 1184 (2x592) | 368 | 640
Scan angle | 56°-44.7° | 44.7°-32° | 32°-0°-32° | 32°-44.7° | 44.7°-56°
Zenith angle | 69.4°-52.6° | 52.6°-36.7° | 36.7°-0°-36.7° | 36.7°-52.6° | 52.6°-69.4°
Bow Tie Line Deletions

## Slide 13
VIIRS M3 band
2013-06-30
06:03:51 UTC
with bowtie deletions filled-in
VIIRS M3 band
2013-06-30
06:03:51 UTC

## Slide 14
VIIRS M3 band
2013-06-30
06:03:51 UTC
VIIRS M3 band
2013-06-30
06:03:51 UTC
rotated so that north is to the top

## Slide 15
VIIRS M3 band
2013-06-30
06:02:26 UTC
VIIRS M3 band
2013-06-30
06:03:51 UTC
Images of two adjacent granules

## Slide 16
VIIRS M3 band
2013-06-30
06:03:08 UTC

## Slide 17: VIIRS scientific units (unlike GOES radiances in RAW counts)
VIIRS bands | Units available from HDF5 via ADDE server (only) |  | Other units in McIDAS
Visible / Reflective | Radiances | Reflectances | Brightness counts
Thermal / Emissive | Radiances | Brightness Temperatures | Brightness counts
Day/Night Band | Radiances | Reflectances | Brightness counts
Best to copy the VIIRS images from the server in the units needed, since once separated from the server, other unit scalings are not automatic, but need to be done manually.

## Slide 18
Three-color (RGB) Product | Red | Green | Blue
True color | M5 (0.672 µm) | M4 (0.555 µm) | M3 (0.488 µm)
Natural color | M10 (1.61 µm) | M7 (0.865 µm) | M5 (0.672 µm)
 | I3 (1.61 µm) | I2 (0.865 µm) | I1 (0.64 µm)
Commonly used three-color (RGB) combinations of VIIRS bands.

## Slide 19
VIIRS true-color RGB combination

## Slide 20
VIIRS natural-color RGB combination
North shore of Black Sea (Odessa)

## Slide 21
VIIRS natural-color image from 24-bit RGB combination (JPG) using COMBINE command

## Slide 22
VIIRS natural-color image from 8-bit RGB combination (GIF) using AREACOLOR program
Northeastern Iraq fires

## Slide 23: Sensor Data Record (SDR) to Environmental Data Record (EDR)
Ground Track Mercator (GTM) remapping software.
  GTM is a remapping of the data, but the same radiances/reflectances/temperatures for Non-NCC bands only.
For NCC imagery, which is derived from the Day Night Band (DNB), there is additional radiance (reflectance) processing
Sensor Data Record (SDR)
Environmental Data Record (EDR)
GTM software
DNB (SDR)
radiance
NCC (EDR) pseudo-albedo
GTM software
plus

## Slide 24: At the Day/Night Terminator
SDR
NCC EDR
11:53 UTC 31 July 2013

## Slide 25: During a New Moon
SDR
NCC EDR
06:43 UTC 6 August 2013
Stray light
Stray light

## Slide 26: NCC Over a Full Lunar Cycle
08:02 UTC 17 July 2013
Lightning
Oil rigs
08:09 UTC 22 July 2013
07:43 UTC 29 July 2013
Moon glint
08:28 UTC 6 August 2013

## Slide 27: Summary
We’ve made excellent progress with VIIRS Imagery after 18 months!
  Various RGB imager products are impressive.
  DNB/NCC Imagery is a great addition to heritage MODIS-type imagery.
McIDAS-X is VIIRS-capable from the server only.
  Offline, VIIRS needs special handling.
  VIIRS geo-locations are inexact for large granule-size images. (not explained here)
McIDAS-V for VIIRS will be addressed by the Mc-V Team.

## Slide 28: BAMS article from the Imagery Team
Hillger, D., T. Kopp, T. Lee, D. Lindsey, C. Seaman, S. Miller, J. Solbrig, S. Kidder, S. Bachmeier, T. Jasmin, and T. Rink, 2013: First-Light Imagery from Suomi NPP VIIRS. Bull. Amer. Meteor. Soc., 94(7), 1019-1029, plus cover images. doi:10.1175/BAMS-D-12-00097.1