## Slide 1: SDI (Satellite Data Ingestor)
2015 McIDAS Users Group Meeting
June 8, 2015

## Slide 2: Overview
SDI 104
  Hardware configuration
  Software configuration
  Satellites signals
Next generation SDI
  Hardware Configuration
  Software configuration
  Satellites signals

## Slide 3
SDI 104
Hardware Configuration
PC/104-Plus
LittleBoard 735
1 GHz CPU
Disk: 160 Gbyte IDE
Boot from compact flash
Ethernet: Up to 1G/s
Connectors for monitor and keyboard
Mounted in 2U rack box

## Slide 4
Hardware Configuration
Data rates tested up to 40 Mbits/s
Connectors:
  D15P
  BNC
Configuration:
  Single ended (TTL)
  RS422 (differential)
Data types
  NRZ-L, NRZ-M, NRZ-S
  Jumper configurable

## Slide 5: Software Configuration
Knoppix 6.7.1 (Linux 3.0.41)
  Up-to-date security
  Compatible with old binaries
  Upgrade to Knoppix for older SDI-104 systems running DSL as needed
  Can be configured as a standalone ingestor/server, or write data to an external disk (via NFS, for example)

## Slide 6
Event Notification
Notifications are dependent on signal type:
  Image start (not for POES)
  Image end (not for GVAR Imager)
Three types of notifications:
  Send an email
  Write notification to a file (log messages)
  Run a program or script

## Slide 7: SDI-104 Status for Current Satellites
GVAR: up-to-date for entire series
MTSAT: up-to-date for both satellites
  May want to add swap space if running DSL (noisy data)
POES AVHRR:
  Up-to-date for all satellites
  Unable to test direct reception, although a system is running at NWS Honolulu

## Slide 8
(Original) SDI Sunset
The Original SSEC SDI was sunset on 31 December 2013
  We are not able to provide nor recommend hardware components if these would fail
  The operating system used is an unsupported version of Solaris, which has been lacking security updates for several years.

## Slide 9
SDI … the next generation

## Slide 10: Introducing the SDI-SE

## Slide 11: SDI-SE Hardware Configuration*
Dell PowerEdge R430 servers
12 core, 2.5 GHz Intel Xeon Processor
64 GB Ram
6 1-TB disks in RAID-6
10 Gb Ethernet and 1 GB Ethernet
  No more clock and data
  Everything over ethernet
(no SSEC designed hardware components)
*preliminary

## Slide 12: SDI-SE Software Configuration*
CentOS 6.x
Software and security updates via yum
  Repository at UW SSEC
McIDAS-X ADDE servers
CSPP-GEO ingest software
RabbitMQ event notification
*preliminary

## Slide 13: SDI-SE Data Access*
ADDE
FTP
*preliminary

## Slide 14: SDI-SE Event Notification*
RabbitMQ
  Built in exchange server
  Start and End Events
  No more email events
  Remote workstations will be able to connect to the Exchange server and receive desired events
  May update SDI-104 to use RabbitMQ in the future
*preliminary

## Slide 15: SDI-SE Supported Satellites *
GOES-R series
  Ingest handled by CSPP GEO
  Instruments
    ABI (Advanced Baseline Imager)
      Follow/tracking
    GLM (Geostationary Lightning Mapper)
    MAG (Magnetometer)
    SEISS (Space Environment In-Situ Suite)
    SUVI (Solar Ultraviolet Imager)
    EXIS (Extreme Ultraviolet and X-ray Irradiance Sensors)
    No Level-2 processing on the SDI-SE
HimawariCast (under consideration)
GVAR (under consideration)
*preliminary

## Slide 16: What is CSPP – GEO?
Community Satellite Processing Package for Geostationary Data
NOAA sponsored project being developed at UW SSEC
The software will be capable of processing GOES Rebroadcast (GRB) data received from the next-generation GOES-R satellite. Level 2 Advanced Baseline Imager (ABI) products will be generated by state-of-the-art science algorithms developed under the GOES-R Algorithm Working Group project.
Software is freely available and is distributed as self-contained binary packages built for 64-bit Linux systems.

## Slide 17: CSPP – GEO initial product suite
Cloud mask
Cloud phase
Cloud type
Cloud top height
Cloud top temperature
Cloud top pressure
Cloud 11 µm emissivity
Cloud visible optical depth
Cloud effective radius
Cloud liquid water path
Cloud ice water path
Probability of Marginal Visual Flight Rules (MVFR)
Probability of Instrument Flight Rules (IFR)
Probability of Low Instrument Flight Rules (LIFR)
Low cloud geometric thickness

## Slide 18
End