## Slide 1: McIDAS – XCD Replacement Update
2016 McIDAS Users’ Group Meeting

## Slide 2: Rewrite Team
Kevin Baggett, Jonathan Beavers, Dan Forrest, Jay Heinzelman, Dave Parker, Jerrold Robaidek, Becky Schaffer, Clayton Suplinski

## Slide 3: McIDAS XCD
McIDAS X
Conventional Data
Decoder
McIDAS-XCD files, decodes and indexes the NOAAPORT data stream into formats that can be served by McIDAS-X ADDE servers.
Output formats include McIDAS MD files, Text files, McIDAS GRID files, GRIB
Version 1 and 2 files, NEXRAD files, and BUFR files.

## Slide 4: NOAAPORT Data
The NOAAPORT broadcast system provides a one-way broadcast communication of NOAA environmental data and information in near-real time to NOAA and external users. This broadcast service is implemented by a commercial provider of satellite communications utilizing C-band.

## Slide 5: NOAAPORT Channels
The following NOAAPORT channels supply data to be decoded by McIDAS-XCD:
NCEP/NWSTG Channel (NWS Telecommunications Gateway)
  model output from the National Centers for Environmental Prediction (NCEP)
  observations, forecasts, watches and warnings from NWS Forecast Offices
  WSR-88D radar products
  most observational data over North America
NCEP/NWSTG2 Channel
  supplements the NWSTG channel

## Slide 6: NOAAPORT Data flow into SSEC
Users generally get NOAAPORT data in two ways:
Directly from DOMSAT (101°W)
Over the Internet via LDM

## Slide 7: Why Replace -XCD?
Installation is difficult
Upgrades are difficult
System is overly complex, large learning curve for operators, and very large learning curve for new programmer
System was written for a mainframe then ported to UNIX
A powerful system is needed to run -XCD, otherwise data can be lost
A data format change can mean bad data, and a fix can be difficult to implement, and is only effective for future data

## Slide 8: Goals
Replace 4 parts of -XCD filing and decoding:
  GRIB
  NEXRAD
  Text
  POINT/MD serving
Utilize LDM direct filing
Reduce or eliminate compiled code
Remove legacy mainframe complexity
Utilize simple open-source database, SQLite
Match or exceed current filing and serving performance on existing hardware

## Slide 9: -XCD Replacement: GRIB Data
LDM files GRIB messages to a temporary directory
A GRIB daemon written in Python watches for data, extracts information and files metadata into a SQLite database
SQLite databases are separated by model and date
Volume of GRIB data has increased greatly over the last several years increasing the challenge

## Slide 10: -XCD Replacement: NEXRAD Data
LDM files NEXRAD files (WSR and TDWR) into a directory structure similar to the existing -XCD Decoder
Data served by NEXRAD server

## Slide 11: -XCD Replacement: Text Data
LDM files data directly to disk
A bash script running as a daemon watches for new data and files data into a daily *.XCD file as data comes in
The bash script extracts metadata for insertion into a daily SQLite database
Text servers (wxtgserv and obtgserv) query SQLite databases to find data and return information to client
Commands: WXTLIST, WWLIST, WWDISP, *RPT

## Slide 12: -XCD Replacement: Point Data
RTPTSRC datasets
Uses certain text data identified by WMO headers filed in the database (e.g. SA and SP for SFCHOURLY)
No MD files are created, but structure created on the fly when serving via ADDE
Commands such as PTLIST, PTDISP and PTCOPY get metadata from the SQLite database, then extract data from the *.XCD file created by the text filer
At the start of each UTC day, a Station Database table (equivalent to STNDB.CORE) is created
Station Database is retained for archived data

## Slide 13: Point Data Improvements
Replacement –XCD captures more surface hourly data than existing –XCD
Existing –XCD: Hourly & 2 Specials
Replacement –XCD: Hourly & All Specials

## Slide 14: Point Data Improvements
Synoptic Data in current –XCD is stored every 3 hours
Replacement –XCD can store every hour

## Slide 15: Point Data Case: Synoptic over Australia
PTDISP RTPTSRC/SYNOPTIC.ALL PAR=T[F] FORMAT=I2 SEL='TIME 12;DAY 2016316' DEC=NO PTDISP RTPTLITE/SYNOPTIC.ALL PAR=T[F] FORMAT=I2 SEL='TIME 12;DAY 2016316' DEC=NO COL=2

## Slide 16: Point Data Case: Synoptic Over Australia
PTDISP RTPTSRC/SYNOPTIC.ALL PAR=T[F] FORMAT=I2 SEL='TIME 12;DAY 2016316' DEC=NO PTDISP RTPTLITE/SYNOPTIC.ALL PAR=T[F] FORMAT=I2 SEL='TIME 12 14;DAY 2016316' DEC=NO COL=2

## Slide 17: Point Data Issues
Number of hourly records of PTCOPY for SFCHOURLY data needs to be increased
  Up to 10 specials per hour?
Number of possible records of PTCOPY for SYNOPTIC data needs to account for the hourly availability

## Slide 18: BUFR Data (Binary Universal FoRmat)
Filed directly using LDM
No operational McIDAS-X server exists
A prototype server was created but has not been updated in several years
Individual files can be loaded into McIDAS-V if they follow the standard BUFR tables
We aim to be ready as BUFR implementation proceeds

## Slide 19: Local Data
A couple -XCD sites have local (non-NOAAport) feeds of data
We have contacted those sites in the past
  So far, no core -XCD decoder dependencies are known i.e. sites have written their own decoders
If there is local data that do depend on -XCD libraries, sites will be able to continue to use -XCD libraries, or may link to McIDAS-X libraries as needed. Contact Jerry Robaidek or Becky Schaffer if you have concerns.

## Slide 20: Hardware Specs
Development hardware (~$4K in 2013)
  2- AMD Opteron 4180 CPUs - 6 core each
  32 GB ram
  7.2k rpm SAS disks
Briefly tested GRIB on a sub $1K desktop
  Intel i5-3570 3.4 GHz (quad core)
  16 GB memory
  7.2k rpm SATA drives (6 Gb/s)

## Slide 21: Serving performance (Text)
TEXT lists
  WXTLIST (no parameters)
    Current -XCD: fastest=.092 s slowest=.105 s
    New -XCD : fastest=.014 s slowest=.35 s
  WXTLIST WMO=SA
    Current -XCD : fastest=.019 s slowest=.259 s
    New -XCD : fastest= 1.654 s slowest= 1.890 s

## Slide 22: Serving performance (SFCRPT)
SFCRPT
  SFCRPT KGRB 9 (Current –XCD)
    Fastest : ~.021 s
    Slowest : ~.419 s
  SFCRPT KGRB 9 (New –XCD)
    Fastest : ~.017 s
    Slowest : ~.122 s

## Slide 23: Serving performance (PTLIST)
PTLIST
  PTLIST RTPTSRC/SFCHOURLY SEL=“DAY 2016312; TIME 12; ID KMSN”
    Current –XCD: fastest=.022 s slowest=.074 s
    New –XCD: fastest=.023 s slowest=.167 s
  Remove ID: PTLIST RTPTSRC/SFCHOURLY SEL=“DAY 2016312; TIME 12”
    New –XCD slows to : ~0.3 s
  Remove ID and Time: PTLIST RTPTSRC/SFCHOURLY SEL=“DAY 2016312”
    New –XCD slows to : ~3.8 s

## Slide 24: Server performance (GRID)
GRID lists (GRDLIST)
  RTGRIDS/GFS-USLC DAY=2016312 TIME=6:00 PAR=U NUM=10
    Current -XCD : ~.45 s
    New -XCD : ~.07 s
GRID display (GRDDISP)
  RTGRIDS/GFS-USLC DAY=2016312 TIME=6:00 PAR=U FHOUR=12 LEV=500
    Current -XCD: ~.185 s
    New -XCD : ~.105 s
GRID copy (GRDCOPY)
  RTGRIDS/NAM-USPS G/G.5700 DAY=2016312 TIME=0:00 PAR=T FHOUR=9 LEV=500
    Current -XCD: ~.125 s
    New -XCD: ~.052 s

## Slide 25: Monitoring
Command line
  ldmadmin watch
  gribadmin
Graphical
  HTML based
  Does not require apache to be installed

## Slide 26: Monitoring

## Slide 27: Point Monitoring

## Slide 28: GRIB Monitoring

## Slide 29: Radar Monitoring

## Slide 30: Packaging and installation
Existing servers and decoders (compiled code) will be migrated into McIDAS-X
We plan to have -XCD replacement beta GRIB software (Python) and text software (bash) packaged as Linux containers using Docker
Docker will simplify the process of building, running, and upgrading the containers
Docker is a relatively new platform and we are working through issues
Goal is to simplify the installation process for system administrators

## Slide 31: Schedule
All ingest and serving components are in testing
Monitoring development and testing in progress
Operations testing in progress
Beta release early 2017
Version 1.0 of the -XCD replacement will be packaged with McIDAS-XCD 2017.1