## Slide 1: University of Wisconsin SSEC
Jerrold Robaidek
Satellite Data Services Program Manager
Datacenter
Satellite Data Services

## Slide 2: SSEC Satellite Data Services Update
SDS Status
SDS Projects

## Slide 3: SSEC SDS
  2 FTE ~100% time
    Computer Operator (1st shift)
    Computer Operator (1st shift)
  5 FTE ~portions of their time
    Program Manager
    System Programmer
    DataBase/Web Programmer
    Research Specialist (PM assistant)
    Antenna/Communication technician
  4 Student QC assistants/programmers (2nd shift)
  Staffed M-F , 7:30 AM - 11:00 pm Central time.

## Slide 4: SSEC SDS
Ops, QC, Programing
  Rosie Spangler, Douglas Ratcliff
QC, Ops, Inventory/Archive, Contracts
  Nancy Troxel-Hoehn
Programmer, UI, DataBase
  Clayton Suplinski
  Staffed M-F , 7:30 AM - 11:00 pm Central time.
Programing, Product Generation, AMQP
  Rick Kohrs
System Programing, Ingestors
  Dan Forrest
Antennas
  Istvan Bocsi

## Slide 5: Data Center Facilities
Over 2100 ft.
The Data Center’s disk storage exceed 12-18 PBs.
The entire room is on four 72 KW UPSs, of which, about 200+ KW are in use. Non UPS power usage is ~17 KW. An additional 72 KW UPS for a smaller 5th floor computer room
Cooling provided by campus chilled water and outside air in the winter. Racks are cooled by 16 in row APC coolers.
Gigabit and 10 Gigabit network (also 100 MB admin network, 40 Gigabit InfiniBand).

## Slide 6: Antennas @ SSEC
C-Band
  11 meter heated (87° West – SES-2, POES Wallops Relay, MSG)
  6.3 meter heated (101° West – SES-1, POES Fairbanks Relay)
  4.5 meter (101° West – SES-1, Noaaport)
  3.7 meter GEONETcast (58º West INTELSAT 21)
L-Band
  7.3 meter (75° West –GOES-East Primary/GOES-16)
  7.3 meter (89.5° West –GOES-West Primary/GOES-17)
  4.6 meter (135° West –GOES-West Primary)
  4.5 meter (135° West –GOES-East auto tracking)
X-Band
  4.4 meter (Tracking – EOS)
X/L Band
  2.4 meter (Tracking – Suomi NPP, EOS, Metop A&B, NOAA-18, 19 and FY3)

## Slide 7: UW SSEC SDS Antennas Remotely Managed
X/L Band
  Honolulu Community College
  Atlantic Oceanographic & Met Lab , Miami, FL
  University of Puerto Rico
  Guam
  All are 2.4 m used for Tracking – Aqua, Terra, Suomi NPP, EOS, Metop A&B, NOAA-18, 19, NOAA-20 and FY3
  Supports
    NOAA NWS NCEP
    Eumetcast
    GTS

## Slide 8: Data Distribution
Realtime
  McIDAS ADDE (Abstract Data Distribution Environment)
  ftp
  http
  Ldm
  Direct access via mount
  WMS (Web map service)
Archive
  ADDE
  Direct Access (in-house only)
  WMS (experimental)
  McFETCH
  THREDDS

## Slide 9: Real-time Data
The SSEC Data Center receives data from 9-12 different geostationary satellites and 12 different polar orbiting satellites. Most data are available in near real-time via ADDE. Other methods of data access are available upon request.

## Slide 10: Geostationary Satellites received
GOES-16 -East (75.2°W)
GOES-15 -West(135°W)
GOES-14 -Test (105°W) (not currently sending)
GOES-17 -Test (89.5°W)
Meteosat-11 (0ºE)
Meteosat-8 (near 41.5°E)
COMS (128ºE)
FY-2E (86°E)
FY-2G (105° E)
Himawari-8 (140° E)
Kalpana(74° E)
INSAT-3D(83° E)

## Slide 11: Geostationary Satellites Received at UW SSEC in 2016
 | Sub-Point | Reception Method | Source | Latency | Daily Volume
GOES-16 | 75.2° West | L-Band | DB | <10 seconds | 130-400 GB
GOES-14 | 105° West | L-Band | DB | <2 minutes | 23 GB
GOES-15 | 135° West | L-Band | DB | <2 minutes | 23 GB
GOES-17 | 89.5ºWest | L-Band | DB | <10 seconds via DB | 130-400 GB
Meteosat-11 | 0° East | C-Band Relay | DB Relay | <15 minutes | 24 GB
Meteosat-8 | 41.5° East | Network Relay | NOAA STAR | ~30 minutes | 24 GB
Himawari-8 | 140° East | Network Relay | NOAA STAR | ~ 10 minutes | 300 GB
Himawari-8 | 140° East | Himawari Cast Network Relay | Hawaii NWS | ~ 10 minutes | 62 GB
Kalpana | 74° East | Network Relay | ISRO | 45-120 minutes | 1.4 GB
Insat-3D | 83° East | Network Relay | ISRO | 45-180 min | 19 GB
FY2E | 86° East | Network Relay | ABOM | 15-30 minutes | 4.7 GB
FY2G | 105° East | Network Relay | ABOM | 15-30 minutes | 4.7 GB
COMS | 128° East | Network Relay | KMA | 9-24 minutes | 11 GB

## Slide 12: Polar Satellites received
NOAA-15
NOAA-18
NOAA-19
NOAA-20 (JPSS-1)
METOP-A
METOP-B
Aqua
Terra
Suomi-NPP
Landsat-8 (RE only)
FY-3B
FY-3C
GCOM-W1
12

## Slide 13: Polar Satellites Received at UW SSEC in 2018
 | Reception Method | Domain | ADDE Latency | Instruments | Access
NOAA-15 | C-Band relay, NOAA-STAR | DB CONUS Global | DB <1 minutes after pass | AVHRR, AMSU, DCS->level-1 | ADDE
 |  |  |  | All other instruments Level-0 | NA
NOAA-18 | DB L-Band, C-Band relay, NOAA STAR | DB CONUS Global | DB <1 minutes after pass | AVHRR->level-1 | ADDE
 |  |  |  | All other instruments Level-0 | NA
NOAA-19 | DB L-Band, C-Band relay, NOAA STAR | DB CONUS Global | DB <1 minutes after pass | AVHRR->level-1 | ADDE
 |  |  |  | All other instruments Level-0 | NA
NOAA-20 | DB XL-Band, NOAA STAR, CLASS | DB CONUS Global | DB <1 minutes after pass | VIIRS>level-1 | ADDE
 |  |  |  | VIIRS,ATMS, CrIS | DB ftp (sips)
Metop-A | DB L-Band, NOAA STAR Relay | DB CONUS Global | CONUS <15 minutes after pass | AVHRR ->level-1 | ADDE
 |  |  |  | AVHRR, IASI | DB ftp (sips)
Metop-B | DB L-Band, NOAA STAR Relay | DB CONUS Global | CONUS <15 minutes after pass | AVHRR ->level-1 | ADDE
 |  |  |  | AVHRR,IASI | DB ftp (sips)
Suomi-NPP | DB X/L Band, NOAA STAR, CLASS | DB CONUS Global | CONUS <15 minutes after pass | VIIRS | ADDE
 |  |  |  | VIIRS,ATMS, CrIS | DB ftp (sips)
Aqua | DB X-Band, NASA Relay | DB CONUS Global | DB <15 minutes after pass | AIRS, MODIS -> Level-1 | ADDE
 |  |  |  | AIRS, MODIS | DB ftp (sips)
Terra | DB X-Band, NASA Relay | DB CONUS Global | DB <15 minutes after pass | MODIS -> Level-1 | ADDE
 |  |  |  | MODIS | DB ftp (sips)
Landsat-8 | Network Relay (USGS) | CONUS | <24 hours | Level-1 | ADDE, WMS
Shizuku GCOM-W1 | DB X-Band | CONUS | DB <1 min after pass | Level-0 | SSEC ftp
FY-3B/C | DB X/L Band | CONUS | DB <1 min after pass | Level-0 | SSEC ftp

## Slide 14: Non-Satellite data
NOAAport
  Text/Point
  Model Grids
  Radar

## Slide 15: Archive Data
As of May 2018, over 1,400 TBs online.
Grows approximately about ~350+ TB/year
US Geostationary Satellites
GOES-8 through GOES-17 (1994-Present) (East, West , South America and test)
GOES-1 through GOES-7 (1978-1996)
SMS-1&2 (1978-1981)

## Slide 16: Archive Data
International Geostationary Satellites
GMS/MTSAT (1998-2015)
Meteosat/Meteosat IODC (1998-Present)
Meteosat-1 FGGE (1978-1979)
FY2 (2004-Present)
Kalpana (2005-2017)
Insat-3D (June 2014-2017)
COMS (June 2012 – Present)
Himawari-8 (March 2015 – Present)

## Slide 17: Archive Data
NOAAPORT/Conventional Data
Model Output (1996-Present)*
In situ Point Observations (1976-Present)

## Slide 18: Other SDS Projects

## Slide 19: McFETCH Satellite Data Server
Dave Parker, Dave Santek, Bill Bellon, Clayton Suplinski, Rick Kohrs, Jerry Robaidek

## Slide 20: McFETCH Satellite Data Server
Multi-format client-agnostic File Extraction Through Contextual HTTP
Allows access to ADDE archive servers
Heavily dependent on McIDAS-X
Outputs all formats McIDAS-X can plus others

## Slide 21: McFETCH Satellite Data Server
Output formats:
AREA | Flat Binary
NetCDF | Gif
Geotiff | JPEG
Flat text | PNG

## Slide 22: McFETCH Satellite Data Server
Access via HTTPS
Any client that can request a URL, can access, subset, and remap satellite data from an ADDE server
Integrated with inventory

## Slide 23: McFETCH Satellite Data Server
Must register for a unique data key
1 GB daily limit
1000 transaction per day daily limit
Data must be 180 days or older (30 Days or older for Unidata Community)

## Slide 24: McFETCH Satellite Data Server

## Slide 25: McFETCH Satellite Data Server

## Slide 26: McFETCH Satellite Data Server

## Slide 27: McFETCH Satellite Data Server

## Slide 28: McFETCH Satellite Data Server

## Slide 29: McFETCH Satellite Data Server

## Slide 30: McFETCH Satellite Data Server

## Slide 31: McFETCH Web Interface

## Slide 32: McFETCH Users
As of May 21, 2018
276 Users
29 users in last 30 days
52,750 transactions in last 30 days

## Slide 33: McFETCH Satellite Data Server
Upcoming updates (summer 2018)
Improved performance for archive requests
Original “archived” format data output

## Slide 34: McFETCH Satellite Data Server
  To get a data access key:
  Go to https://mcfetch.ssec.wisc.edu

## Slide 35: McIDAS in Python
Uses code developed by Kevin Hallock and Jon Beavers
New McIDAS scripts in Python
Available in McIDAS 2017.1 XRD

## Slide 36: AMQP RabbitMQ
AMQP -> Advanced Message Queuing Protocol
RabbitMQ
amqpfind
Himawari
GOES-16/17
Expand to other GEOs and Polar

## Slide 37: GRB Fanout server
Developed by Dan Forrest

## Slide 38: GRB Fanout Server
The Problem:
Quorum Demodulator
  Single UDP stream
  Multicast broadcast
Multiple Ingestors needed GRB stream
Not all Co-located
Multicast through router data loss
Development planned in 2015
Only SDS/Datacenter funds were used for this.
Quorum GRB-200 Demodulator

## Slide 39: GRB Fanout Server
AWS Cloud
GRB-200 Demodulator
Network
switch/router
UW SSEC
SDI appliance
Fanout
server
UW SSEC
CSPPGEO
UW SSEC
inge
GRB
UDP
TCP/IP
31 Mbps
n X 31 Mbps
31 Mbps
31 Mbps
31 Mbps
31 Mbps
internet
Remote CSPP
ingestor
2 x 31 Mbps
31 Mbps
Unidata in Boulder
Remote CSPP
ingestor
31 Mbps

## Slide 40: Fanout server hardware specs
Dell PE R430
Single Intel Xeon 2.4GHz 6 core processor
8GB RAM
2TB disk (2 x 200GB & 1 x 1.6TB)
$3,600 USD

## Slide 41: GRB Fanout Server
Compatible with CSPP-GEO, SDI GRB Appliance
Still in “ALPHA”
Need additional resources to move to mature distribution

## Slide 42: GRB Fanout switching
Sometimes you need to switch to a different fanout server due to:
  Swapping Antennas
  Swapping demodulators
  Antenna down time (planned or unplanned)
  Local RFI (E.g. Solar RFI)

## Slide 43: GRB Mixer
Developed by Dan Forrest

## Slide 44: GRB Mixer
Allows mixing of 1 or more fanout feeds …. automatically
Mix feeds at the “CADU” level
Great solution for local Radio Frequency Interference mitigation

## Slide 45: GRB Fanout Server with Mixer
AWS Cloud
GRB-200 Demodulator
Network
switch/router
UW SSEC
SDI appliance
Fanout
server
UW SSEC
CSPPGEO
UW SSEC
inge
GRB
UDP
TCP/IP
31 Mbps
n X 31 Mbps
31 Mbps
31 Mbps
31 Mbps
31 Mbps
internet
Remote CSPP
ingestor
2 x 31 Mbps
31 Mbps
Unidata in Boulder
Remote CSPP
ingestor
31 Mbps

## Slide 46: Fanout and Mixer in the Cloud
GRB-200 Demodulator
Network
switch/router
AWS Cloud
UW SSEC
SDI appliance
Fanout/mixer
server
UW SSEC
CSPPGEO
UW SSEC
inge
Fanout & Mixer
server
CSPP
CSPP
Fanout/mixer
server
Fanout/mixer
server
Fanout/mixer
server
Fanout/mixer
server
Fanout/mixer
server

## Slide 47: GRB Mixer
Great for RFI!
Some RFI Sources
  Solar (annually near equinox)
  Local terrestrial … Powerlines, stray RF
  Lightning

## Slide 49: Solar RFI Graphs

## Slide 50: Solar RFI at PDA ground station March 5, 2018
03/05/2018 17:06:38 - 17:15:57 UTC
Affected 7 Meso-scale sectors
  5 entire images lost
  2 partial images
Affected 1 Full Disk
  8 Channels partial loss
  8 channels No loss
Affected 1 CONUS (all 16 channels lost)
PDA
SSEC

## Slide 51
SSEC

## Slide 52: RFI due to Lightning
Lightning Flash
4.3 Miles away
SSEC Antenna
Location
Lightning Flash occurred at 22:36:36Z on March 5, 2018

## Slide 53: BCH* UnCorrectable
*Bose–Chaudhuri–Hocquenghem

## Slide 54: RFI Due to Lightning

## Slide 55: What about GVAR?

## Slide 56: RFI due to Lightning (May 3, 2018 00:37 UTC)
SSEC Antenna
Location
Lightning event at 00:35 - 00:40Z on May 3, 2018

## Slide 57: BCH* UnCorrectable
*Bose–Chaudhuri–Hocquenghem
Right Hand Circular Polarized (RHCP)
Left Hand Circular Polarized (LHCP)

## Slide 58: RFI Due to Lightning
CONUS
May 3, 2018
00:37:22 UTC
Antenna Only
2 Antennas through Mixer

## Slide 59: RFI Due to Lightning
Meso 1
May 3, 2018
00:38:30 UTC
2 Antennas through Mixer
Antenna Only

## Slide 60: RFI Due to Lightning
Full Disk
May 3, 2018
00:30:41 UTC
2 Antennas through Mixer
Antenna Only

## Slide 61: GRB Mixer
Compatible with CSPP-GEO, SDI GRB Appliance
Still in “ALPHA”
Need additional resources to move to mature distribution

## Slide 62: ABI Monitor

## Slide 63: ABI Monitor

## Slide 64: ABI Monitor

## Slide 65: ABI Monitor

## Slide 66: ABI Monitor

## Slide 67: ABI Monitor

## Slide 68: ABI Monitor
Statistics
January 1 through May 13, 2018.

## Slide 69: ABI Monitor
Statistics
March 4 through May 13, 2018.

## Slide 70: ABI Monitor
Uses McFETCH
Generic image QC code
All GEOs planned to be added to a QC monitor

## Slide 71: Data Access Page
Real-time Data

## Slide 72: Data Access Page
Archive Data

## Slide 73: GEONETcast
Used to monitor polar data uplinks

## Slide 74: GEONETcast

## Slide 75: Cloud initiatives
McIDAS client container
McIDAS ADDE server container
Fanout server container

## Slide 76
Questions?