## Slide 1: University of Wisconsin SSEC
McIDAS Users Group Meeting
September 16-17, 2019
Satellite Data Services Update

## Slide 2: SSEC SDS
  SDS operations and QC lead
  Senior Systems Programmer
  Senior Research Application Programmer
  Visualization, Database, and Web programmer
  Research Intern
  Program manager
  Antenna/Communication technician
  3 Student QC assistants/programmers
  Staffed M-F , 8:30 AM - 5:00 pm Central time.

## Slide 3: Retirements
Rosie Spangler (33 years)
Nancy Troxel-Hoehn (30 years)

## Slide 4: Data Center Facilities
Over 2100 ft.
The Data Center’s disk storage exceed 15-20 PBs.
The entire room is on four 72 KW UPSs, of which, about 200+ KW are in use. Non UPS power usage is ~17 KW. An additional 72 KW UPS for a smaller 5th floor computer room
Cooling provided by campus chilled water and outside air in the winter. Racks are cooled by 16 in row APC coolers.
Gigabit and 10 Gigabit network (also 100 MB admin network, 40 Gigabit InfiniBand).

## Slide 5: Data Center Facilities
UW Provisioned Off-site Data Center
Tier 3, backup power, cooling
Essential systems
Ingest, Distribution
On UW network
Plans to expand for projects that demand high availability

## Slide 6: S4 Super Computer
Funded in 2018 by NOAA
2,560 cores
  15 TB memory
  4 PBs of storage
  Researching satellite data assimilation into operational NOAA models
  This is the 3rd enhancement(2011,2013)

## Slide 7: SSEC Data Center Incoming Data October, 2018
1,033+ GB/day
via Satellite
(C-band. L-band, X-band)
7,330+ GB/day
via Internet*
(ftp, LDM, ADDE, http)
GOES satellites ~690 GB/day
International Geo Satellites ~500+ GB/day
NOAA 15-19 Polar ~27 GB/day
Landsat-8 ~50 GB/day
MODIS polar ~150 GB/day
SUOMI NPP (VIIRS CrIS ATMS) 3,400+ GB/day
Noaaport, GNC-A, misc* 3,700+ GB/day
* Some data are duplicates pulled from multiple sources
CIMSS & SSEC at the UW-Madison
CIMSS = Cooperative Institute for Meteorological Satellite Studies
SSEC = Space Science &Engineering Center

## Slide 8: Antennas @ SSEC
C-Band
  11 meter heated (101° West – SES-1, POES Fairbanks Relay )
  6.3 meter heated (87° West – SES-2, POES Wallops Relay)
  4.5 meter (101° West – SES-1, Noaaport)
  3.7 meter GEONETcast (58º West INTELSAT 21)
L-Band
  7.3 meter (75° West –GOES-East Primary/GOES-16)
  7.3 meter (137° West –GOES-West Primary/GOES-17)
  4.6 meter (128° West –GOES-15)
  4.5 meter (60° West –GOES-13/GOES-14/GOES-15 backup )
X-Band
  4.4 meter (Tracking – EOS)
X/L Band
  2.4 meter (Tracking – Suomi NPP, EOS, Metop A&B, NOAA-18, 19, 20 and FY3)

## Slide 9: UW SSEC SDS Antennas Remotely Managed
X/L Band
  Honolulu Community College
  Atlantic Oceanographic & Met Lab , Miami, FL
  University of Puerto Rico
  Guam
  All are 2.4 m used for Tracking – Aqua, Terra, Suomi NPP, EOS, Metop A,B&C, NOAA-18, 19, NOAA-20 and FY3
  Supports
    NOAA NWS NCEP
    Eumetcast
    GTS

## Slide 10: Real-time Data
The SSEC Data Center receives data from 10+ different geostationary satellites and 13+ different polar orbiting satellites. Most data are available in near real-time via ADDE. Other methods of data access are available upon request.

## Slide 11: Geostationary Satellites received
GOES-16 -East (75.2°W)
GOES-15 -West(128°W)
GOES-13/14 -Test (141º/104ºW)
GOES-17 -West(137°W)
Meteosat-11 (0ºE)
Meteosat-8 (near 41.5°E)
COMS (128ºE) *
FY-2H (79°E)
FY-2G (99.5° E)
Himawari-8 (140° E)
FY-4A GIIRS only(105° E)
INSAT-3D(83° E)
*GEO-KOMPSAT-2A being pursued

## Slide 12: Geostationary Satellites Received at UW SSEC in 2019
 | Sub-Point | Reception Method | Source | Latency | Daily Volume
GOES-16 | 75.2° West | L-Band | DB | <10 seconds | 130-400 GB
GOES-13/14 | 141°/104º West | L-Band | DB | <2 minutes | 23 GB
GOES-15 | 128.5° West | L-Band | DB | <2 minutes | 23 GB
GOES-17 | 137ºWest | L-Band | DB | <10 seconds | 130-400 GB
Meteosat-11 | 0° East | Network Relay | NOAA STAR | ~30 minutes | 24 GB
Meteosat-8 | 41.5° East | Network Relay | NOAA STAR | ~30 minutes | 24 GB
Himawari-8 | 140° East | Network Relay | NOAA STAR ABOM (backup) | ~ 10 minutes | 300 GB
Himawari-8 | 140° East | Himawari Cast Network Relay | Hawaii NWS | ~ 10 minutes | 62 GB
FY2H | 79° East | Network Relay | ABOM | 15-30 minutes | 4.7 GB
FY2G | 99.5° East | Network Relay | ABOM | 15-30 minutes | 4.7 GB
COMS | 128° East | Network Relay | KMA | 9-24 minutes | 11 GB
FY-4A (GIIRS only) | 105º East | Terrestrial Eumetcast | Eumetsat | 10-15 minutes | ~5 – 13 GB

## Slide 13: Polar Satellites received
NOAA-15
NOAA-18
NOAA-19
NOAA-20 (JPSS-1)
METOP-A
METOP-B
METOP-C
Aqua
Terra
Suomi-NPP
Landsat-8 (RE only)
FY-3B
FY-3C
GCOM-W1
13

## Slide 14: Polar Satellites Received at UW SSEC in 2019
 | Reception Method | Domain | ADDE Latency | Instruments | Access
NOAA-15 | C-Band relay, NOAA-STAR | DB CONUS Global | DB <1 minutes after pass | AVHRR, AMSU, DCS->level-1 | ADDE
 |  |  |  | All other instruments Level-0 | NA
NOAA-18 | DB L-Band, C-Band relay, NOAA STAR | DB CONUS Global | DB <1 minutes after pass | AVHRR->level-1 | ADDE
 |  |  |  | All other instruments Level-0 | NA
NOAA-19 | DB L-Band, C-Band relay, NOAA STAR | DB CONUS Global | DB <1 minutes after pass | AVHRR->level-1 | ADDE
 |  |  |  | All other instruments Level-0 | NA
NOAA-20 | DB XL-Band, NOAA STAR, CLASS | DB CONUS Global | DB <1 minutes after pass Global network relay ~45 min | VIIRS>level-1 | ADDE
 |  |  |  | VIIRS,ATMS, CrIS | DB ftp (sips)
Metop-A/B/C | DB L-Band, NOAA STAR Relay | DB CONUS Global | CONUS <15 minutes after pass | AVHRR ->level-1 | ADDE
 |  |  |  | AVHRR, IASI | DB ftp (sips)
Suomi-NPP | DB X/L Band, NOAA STAR, CLASS | DB CONUS Global | CONUS <15 minutes after pass Global network relay ~45 min | VIIRS | ADDE
 |  |  |  | VIIRS,ATMS, CrIS | DB ftp (sips)
Aqua | DB X-Band, NASA Relay | DB CONUS Global | DB <15 minutes after pass | AIRS, MODIS -> Level-1 | ADDE
 |  |  |  | AIRS, MODIS | DB ftp (sips)
Terra | DB X-Band, NASA Relay | DB CONUS Global | DB <15 minutes after pass | MODIS -> Level-1 | ADDE
 |  |  |  | MODIS | DB ftp (sips)
Landsat-8 | Network Relay (USGS) | CONUS | <24 hours | Level-1 | WMS
Shizuku GCOM-W1 | DB X-Band | CONUS | DB <1 min after pass | Level-0 | SSEC ftp
FY-3B/C | DB X/L Band | CONUS | DB <1 min after pass | Level-0 | SSEC ftp

## Slide 15: Data Distribution
Realtime
  McIDAS ADDE (Abstract Data Distribution Environment)
  ftp
  http
  LDM
  Direct access via mount (in-house only)
  WMS (Web map service)
Archive
  ADDE
  Direct Access (in-house only)
  WMS (experimental)
  McFETCH
  THREDDS

## Slide 16: Non-Satellite data
NOAAport (500+GB/day)
  Text/Point
  Model Grids
  Radar

## Slide 17: Archive Data
As of May 2019, over 1,700 TBs online.
Grows approximately about ~350+ TB/year
US Geostationary Satellites
GOES-8 through GOES-17 (1994-Present) (East, West , South America and test)
  G16 and G17 L1 ABI and L2 GLM in Netcdf
  G16 and G17 CADUs (essential for SDS and CSPP-GEO debugging)
GOES-1 through GOES-7 (1978-1996)
SMS-1&2 (1978-1981)

## Slide 18: Archive Data
International Geostationary Satellites
GMS/MTSAT (1998-2015)
Meteosat/Meteosat IODC (1998-Present)
Meteosat-1 FGGE (1978-1979)
FY2 (2004-Present)
Kalpana (2005-2017)
Insat-3D (June 2014-2017)
COMS (June 2012 – Present)
Himawari-8 (March 2015 – Present)

## Slide 19: Archive Data
NOAAPORT/Conventional Data
Model Output (1996-Present)*
In situ Point Observations (1976-Present)

## Slide 20: SDS related initiatives
AMQP Events
Satellite QC API
GRB Fanout/Mixer
Other projects

## Slide 21
AMQP status
AMQP == Advanced Message Queuing Protocol
Provides end user notification of data events
Python program amqpfind
Allows end user better reliability, shorter latencies
Will run both at SSEC and at remote Datacenter (eventually the cloud?)
Will move to as many datasets as possible/practical
Publisher
Messaging
Queue
image start
band end
image complete
Client
http://www.ssec.wisc.edu/datacenter/amqpfind

## Slide 22
AMQP status
Publisher
Messaging
Queue
image start
band end
image complete
Client
http://www.ssec.wisc.edu/datacenter/amqpfind
Satellites
GOES-16/17
    L1b - all instruments
    GLM
    L2 products
Himawari (HDS)
NOAA-20 (VIIRS only)
SNPP (VIIRS only)

## Slide 23
AMQP status
Publisher
Messaging
Queue
image start
band end
image complete
Client
http://www.ssec.wisc.edu/datacenter/amqpfind
Python requirements
  Multi-server: Python 2.7 and greater Single Server: Python 2.6 and greater
Tested operating systems
  Redhat/CentOS 6 and 7 OS X 10.0

## Slide 24: Satellite QC API
https://qcweb.ssec.wisc.edu/web/abi_quality_scores/

## Slide 25: Satellite QC API
https://qcweb.ssec.wisc.edu/web/abi_quality_scores/#values:latency;

## Slide 26: Satellite QC API

## Slide 27: Satellite QC API
Will migrate all GEOs to API first
Integrated with inventory
Will eventually add Non-GEOs
Public accessible interface

## Slide 28: Fanout/Mixer Server
Fanout allows:
  Transmission of GRB CADU/CCSDS packets via TCP/IP
  Distribution of GRB via internet
  Feed multiple ingestors without using multicast

## Slide 29: Fanout/Mixer Server
Mixer allows:
  Multiple antenna inputs
  Mix feeds at the “CADU” level
  Can allow selective data distribution
  Great for RF interference mitigation
  Automatic redundancy

## Slide 30: Solar RFI at PDA ground station March 5, 2018
03/05/2018 17:06:38 - 17:15:57 UTC
Affected 7 Meso-scale sectors
  5 entire images lost
  2 partial images
Affected 1 Full Disk
  8 channels partial loss
  8 channels No loss
Affected 1 CONUS (all 16 channels lost)
PDA
SSEC

## Slide 31: Fanout/Mixer Server

## Slide 32: Fanout/Mixer Server

## Slide 33: Other projects
GOES-17 detector cooling problem imagery mitigation (Fusion)
  Mission-level netCDF are created experimentally
FY-4A GIIRs checkout
Outreach activities
  Climate digest
  Virtual Reality (VR) demos

## Slide 34: Thanks!