## Slide 1: RealEarth
David Parker
MUG Meeting - Sep 2023

## Slide 2: RealEarth
Overview
RealEarth
Conceived as a way for scientists at SSEC to easily visualize the output of their work
Built on open-source GIS tools to enable visualization of mixed-resolution geolocated raster and vector data (images and shapes)

## Slide 3: RealEarth
Overview
RealEarth
Conceived as a way for scientists at SSEC to easily visualize the output of their work
Built on open-source GIS tools to enable visualization of mixed-resolution geolocated raster and vector data (images and shapes)
Allows easy colocation of products in time and space
Supports pan/zoom and animation
Default viewer is flat Leaflet slippy map, Cesium globe view is optional, etc.
API endpoints for easy access

## Slide 4: RealEarth
Head Nodes
Redundant HAProxy backends
Expandable
Interchangeable
haproxy: realearth.ssec.wisc.edu
re1
frontend
(primary 1)
database
(primary)
haproxy: realearth.ssec.wisc.edu
re2
frontend
(primary 2)
database
(backup)
https://realearth.ssec.wisc.edu

## Slide 5: RealEarth
Data Nodes
15 hosts
  24-48 cores
  64-128gb memory
  Many TBs disk
22 Identical VMs serving RealEarth products
  Provisioned as necessary
Nine product generation VMs
karben4
fantasy
(node 1)
brewery
(production)
luck
(node 2)
lakelouie
warped
(node 1)
brewery
(production)
mephisto
(node 2)
capital
skal
(node 1)
brewery
(production)
mutiny
(node 2)
… many more…

## Slide 6: RealEarth
Data Nodes
15 hosts
  24-48 cores
  64-128gb memory
  Many TBs disk
22 Identical VMs serving RealEarth products
  Provisioned as necessary
Nine product generation VMs
karben4
fantasy
(node 1)
brewery
(production)
luck
(node 2)
lakelouie
warped
(node 1)
brewery
(production)
mephisto
(node 2)
capital
skal
(node 1)
brewery
(production)
mutiny
(node 2)
… many more…

## Slide 7: RealEarth
Federation
karben4
fantasy
(node 1)
brewery
(production)
luck
(node 2)
lakelouie
warped
(node 1)
brewery
(production)
mephisto
(node 2)
capital
skal
(node 1)
brewery
(production)
mutiny
(node 2)
… many more…
User requests - Session round-robin
realearth.ssec.wisc.edu
re1: frontend
(primary 1)
re2: frontend
(primary 2)
SSL, sessions, cache, etc
HAProxy
Grafana stats
API calls

## Slide 8: RealEarth
Products
>1,100 products
26 collections
139 categories
Product List
Admin Overview
{
"id": "globalir",
"dataid": "globalir",
"duplicate": false,
"reingest": false,
"name": "Global Infrared",
"description": "This product is a global composite of imagery from multiple satellites. It is completed every hour (at about 35-minutes after the hour UTC) by the SSEC Data Center with the best available imagery. While it shows the most current imagery, shifting occurs along composite seams.",
"owner": "",
"url": "",
"categories": [
"Global"
],
"order": 0,
"orderclause": "",
"opacity": 100,
"type": "raster",
"displaytype": "tile",
"projection": "epsg:4326",
"marker": "",
"probe": "value",
"units": "C",
"maxzoom": 7,
"seedpolicy": 6,
"seedlatbound": 85,
"static": false,
"released": true,
"status": 0,
"optimizeflag": 0,
"fetch": false,
"centerproperty": null,
"declutter": true,
"cluster": true,
"declutterexempt": null,
"outputtype": "png24",
"resample": "nearest",
"processing": "",
"scalemin": "0",
"scalemax": "0",
"minutes": "90",
"timewindow": "0",
"showlegend": true,
"merge": "none",
"mergeproducts": "",
"times": [],
"notifyvalues": [],
"hasparts": false,
"largetiles": true,
"vmid": "e1131cfda86d389c99420e42766ecdc2"
},

## Slide 9: RealEarth
Usage
>6 billion hits
~1.15m unique IPs
Live Usage
Admin Activity

## Slide 10: Product Creation
Breweries - Polling
Cron entries trigger McIDAS-X processing
Legacy VM dating from 2009
Russ Dengel wrote a LOT of code—including custom FORTRAN McX commands—to create product imagery from SDS holdings

## Slide 11: Product Creation
Breweries - Polling
Cron entries trigger McIDAS-X processing
Legacy VM dating from 2009
Russ Dengel wrote a LOT of code—including custom FORTRAN McX commands—to create product imagery from SDS holdings
The spirit of PAW lives on!

## Slide 12: Product Creation
Breweries - RabbitMQ
AMQPFind listens for new data messages
Himawari, ABI, VIIRS
Trigger processing on message reception
  Pass to Python script to parse payload dictionary
  Launch McX mcenv session to fetch and process data

## Slide 13: Product Creation
Breweries - RabbitMQ
AMQPFind listens for new data messages
Himawari, ABI, VIIRS
Trigger processing on message reception
Queueing with separate process thread
  Don’t miss messages
  Avoid saturating resources

## Slide 14: Product Creation
Breweries - McIDAS-X
Running on every single RealEarth VM in the federation
Integral part of product generation for 100s of products
Can accept AREAs as input
GeoTIFF writer creates rasters that are ingested directly
CSV vector data converted to GeoJSON for ingest

## Slide 15: Product Creation
Breweries - Scrape & Fetch
PHP and Python classes to manage remote data mirroring
  FTP
  HTTP(S) w/auth
  Local directory
Custom processing using GDAL, Python, and shell scripts

## Slide 16: Product Creation
External Sources
External users can create and manage products
520 external users registered as product managers
Can upload using a shell script or web form
Happy to help anyone set up a user account

## Slide 17: Data Ingest
Raster Imagery
GeoTIFF format (also COG)
Overviews added for all zoom levels
Tiles are optionally pre-seeded for better performance
Multi-band, multi-byte
Enhancements can be added to 1-byte data

## Slide 18: Data Ingest
Raster Imagery
GeoTIFF format (also COG)
Overviews added for all zoom levels
Tiles are optionally pre-seeded for better performance
Multi-band, multi-byte
Enhancements can be added to 1-byte data
Band combinations
Calibrated data values

## Slide 19: Data Ingest
Raster Imagery
GeoTIFF format (also COG)
Overviews added for all zoom levels
Tiles are optionally pre-seeded for better performance
Multi-band, multi-byte
Enhancements can be added to 1-byte data
Transparency masking
Variable opacity
Honor NODATA

## Slide 20: Data Ingest
Vector Imagery
GeoJSON format
Can be viewed as shape objects (point, line, polygon) or rendered into tiles (raster)
Points can be rendered using Canvas drawing techniques

## Slide 21: Data Ingest
Time Steps
Each time step is unique
Data for each time step can be split and uploaded as a "part" and merged geospatially on the fly
Time steps can be aggregated through time into a single display
"Time" dimension was a novel idea for GIS in 2009

## Slide 22: Data Ingest
mapserver
https://mapserver.org/
OGR-compliant web mapping server
Speaks WMS/WMTS/WFS, etc. to GIS clients
mapscript API for fine-grain control
GDAL tools used for data translation and mapping

## Slide 23: Data Ingest
mapserver
https://mapserver.org/
OGR-compliant web mapping server
Speaks WMS/WMTS/WFS, etc. to GIS clients
mapscript API for fine-grain control *
GDAL tools used for data translation and mapping
key feature
Each time step is a Layer
Time steps are transient
Allows aggregate sources
Dynamic band combinations

## Slide 24: Data Volume
Incoming
Tens of 1,000s of time steps per hour
  GOES-16 alone accounts for ~4,300 individual time steps per hour
Each product defines a data cylinder based on # of time steps or absolute time range
  Some keep months of 1-min data

## Slide 25: Data Volume
Outgoing
Steady 1.5 - 2 million requests served each day
Spikes to 3+ million during severe weather events
Embedded and used around the world
  Hobby websites
  State agencies in the Americas and Asia

## Slide 26: Project Support
Distinct uses at SSEC
Non-federated instances of RealEarth
Separate authentication and access

## Slide 27: Project Support
Distinct uses at SSEC
Non-federated instances of RealEarth
Separate authentication and access
Boeing
Global flood monitoring
Cloud product development
GEONETCast (GNC-A)
ProbSevere LightningCast
MyRadar
Fire detection

## Slide 28: Wildfires
Case Study
Integrate GIS data with satellite observations

## Slide 29: Wildfires
Case Study
Integrate GIS data with satellite observations
Land cover and fuel type
LANDFIRE

## Slide 30: Wildfires
Case Study
Integrate GIS data with satellite observations
Land cover and fuel type
Fire perimeters
NIFC

## Slide 31: Wildfires
Case Study
Integrate GIS data with satellite observations
Land cover and fuel type
Fire perimeters
Fire detection pixels
Histogram of land cover and fuel types
NGFS

## Slide 32: Wildfires
Case Study
Integrate GIS data with satellite observations
Land cover and fuel type
Fire perimeters
Fire detection pixels
Histogram of land cover and fuel types
Solar farm identification

## Slide 33: RealEarth
Live Demo
Basic
Globe
Basemaps, Labels, Other controls (share, draw, etc.)
Station models
Probe & Feature tracking
Parts / Time aggregation