## Slide 1: Calibration and Validation of FY-3D Optical Sensors MERSI-II and HIRAS
Xiuqing Hu,
Na Xu, Chenli Qi, Hanlie Xu, Chunqiang Wu，
Lin Chen, Ling Wang, Ronghua Wu, Ling Sun, Peng Zhang
National Satellite Meteorological Center,
China Meteorological Administration
(NSMC/CMA)
2019 CSPP June 25-27, Chengdu, China

## Slide 2
Outline
Overview of FY-3D optical sensors
MERSI-II Cal/Val
HIRAS Cal/Val
Mutual Evaluation of MERSI-II and HIRAS
MERSI-II Products Demonstration
Summary

## Slide 3: Background of FY-3X serial satellite
FY-3 is the Chinese second generation LEO meteorological satellite.
Four Satellites has already been on orbit and four more satellite will be lunched.
2008.05.27 | FY-3A | AM
2010.11.05 | FY-3B | PM
2013.09.23 | FY-3C | AM
2017.11.15 | FY-3D | PM

## Slide 4
10 instruments on board FY-3D:
5 Successive instruments:
MWTS-II: Microwave Temperature sounder
MWHS-II: Microwave Humidity sounder
MWRI: Microwave Radiation Imager
GNOS: Global Navigation Occultation Sounder
SEM: Space Environment Monitor
2 Improved instruments：
MERSI-II：Improved from MERSI
HIRAS: Upgraded from filter-type sounder IRAS
3 New Instruments:
GAS: Greenhouse gases Absorption Spectrometer
WAI: Wide-angle Aurora Imager
IPM: Ionospheric Photometer
FY-3D Instrument configuration -- Launched on 15, Nov. 2017 and commissioning almost finished
FY-3D
FY-3A/B/C

## Slide 5: Imager of FY-3D: MERSIMERSI-II Continuity and Evolution
MERSI-II Improvement:
  Cover all bands in FY-3A/B/C MERSI
  Five more IR bands with 2 split windows with 250m spatial resolution
  Add Circurrus cloud band 1.38um
  Water vapor bands In NIR and 7.2um
  Higher accuracy using onboard calibrator
  Lunar Calibration capability
MERSI-II global Mosaic image
MERSI-II global AOD over land

## Slide 6: MERSI-II improvements from MERSI
More Baffle to decrease straylight contamination: have been installed on the head of the instrument to further prevent contamination from solar illumination.
OBCBB structure improvements to enhance emissivity and temperature uniformity, new capability on warm up and cool down (WUCD)
New capability for Moon Observation Maneuver: By changing the scan timing sequence, MERSI II has a moon observation mode, which can achieve the initiative moon observation and calibration ability.
RSB VOC improvements to reduce self-degaradation: To minimize SIS degradation and its associated effects due to solar exposure, a shutter door is mounted on the solar incident light cone and is kept closed except during solar calibration events. The spectra of the standard trap detectors are also adjusted to better characterize changes in MERIS RSBs.
Notes: Overall, many design improvements have been applied in MERSI II, laying the foundation for better on-orbit performance and measurement.
more Baffle to decrease straylight contamination: have been installed on the head of the instrument to further prevent contamination from solar illumination.
structure improvements and WUCD capability on OBCBB:The structure of the MERSI II OBCBB is optimized to enhance emissivity and temperature uniformity. The thickness has been increased from 8 mm to 25 mm, and the V-groove included angle has decreased from 45° to 30°, which increases the effective emissivity from approximately 0.94 to >0.97. The MERSI II OBCBB, which is normally controlled at a fixed temperature, has been redesigned with the capability to warm up and cool down (WUCD) via several heating elements.
New capability for Moon Observation Maneuver: By changing the scan timing sequence, MERSI II has a moon observation mode, which can achieve the initiative moon observation and calibration ability.
VOC improvements to reduce self-degaradaiotn :To minimize SIS degradation and its associated effects due to solar exposure, a shutter door is mounted on the solar incident light cone and is kept closed except during solar calibration events. The spectra of the standard trap detectors are also adjusted to better characterize changes in MERIS RSBs.

## Slide 7: Moon view and calibration
Unschedule
Schedule
Absolute Calibration
Degradation monitoring
Interband Calibration
Notes: Moon calibration
  mainly based on unscheduled observation monthly
  absolute and interband calibration
  degradation monitoring

## Slide 8: IR Hyperspectral HIRAS
Band | Spectral range (cm-1) | Resolution (cm-1) | NET @250K | chs
Longwave | 650 *– 1136 （15.38 m-8.8 m） | 0.625 | 0.15K | 778
Midwave1 | 1210 – 1750 （8.26m-5.71 m） | 1.25 | 0.1K | 433
Midwave2 | 2155-2550 （4.64m-3.92 m） | 2.5 | 0.3K | 159
HIRAS is a great improvement to Chinese satellite infrared atmospheric sounding system

## Slide 9: FY-3D Commissioning and Operational Phase
In-orbit delivery for trial operation
July
2018
31st June
2018
Complete summary and review of the orbit test
Turn into formal operation and data release
August
2018
Oct.
2018
Complete the orbital check out
15 November
2017
lunched successfully

## Slide 10: MERSI/HIRAS Cal/Val using GSICS
Spectral calibration, radiometric calibration and geolocation accuracy of FY-3D MERSI-II and HIRAS including the was conducted using GSICS platform at CMA GSICS research processing center (GPRC). The GSICS-consensus reference instruments IASI, CrIS, MODIS and VIIRS are used to evaluate the radiometric accuracy of MERSI-II and HIRAS.
Accurate collocation and inter-comparison between MERSI-II and HIRAS at the same satellite platform FY-3D gave us several important information of their performance, especially the knowledge of HIRAS subpixel geolocation shift.
Based on the above GSICS evaluation, mechanism behind radiometric calibration bias of MERSI-II and HIRAS also were found including the non-linearity, polarization effect and other parameters of the instruments. These parameters were updated several times based on comprehensive assessment and iterative validation during the commissioning test.

## Slide 11: CMA GSICS Platform
All kinds of data are collected to perform Wide Dynamic calibration based on CMA GSICS GPRC
Global deserts
SNO
SNOx

## Slide 12: MERSI-II TEB Validation using SNO IASI and CrIS
Band 25
Band 22
Band 23
Band 24
Band 20
IR calibration bias and stability monitoring Using Metop-B IASI reference
TB Bias@250K is about 0.5K~1K based on prelaunch BB emissivity and nonlinear parameter

## Slide 13
Find the calibration bias mechanism and Update the calibration parameters based on the GSICS evaluation
8.5m
MERSI TEBs calibration
update procedure
SNO Samples collection
Evaluation calibration bias
Update the calibration model
Validation using new samples

## Slide 14: TEB Calibration update based on GSICS Evaluation
MERSI-HIRAS Inter-comparison（April~Sep.,2019）
Old Model New Model

## Slide 15: MERSI-II SRB Cal/Val methods
Reflectance Dynamic | Method | Comparison | Applicable channels of MERSI II
High（>80%） | DCC | Merit：high stability, providing high brightness information, better performance in the absorption channel Demerit：saturation in ocean channels | 1~7，16~19
Medium（<80%） | Multi-Site | Merit：multi-targets Demerit：seasonal variation affected by atmosphere and surface, unsuitable for absorption channels | 1~19
 | SNO_GOME | Merit： not rely on the atmosphere and surface observation, spectral differences can be ignored, providing medium reflectance targets for ocean channels; Demerit：Only suit for VIS channels | 1~3，8~15
 | SNO_MODIS | Merit：Do not rely on the atmosphere and surface observation Demerit：Need spectral correction | 1~18
 | SNO_VIIRS |  | 2~10、12、14、15
Low（<10%） | Moon | Merit：High stability Demerit：Accuracy depending on the moon model, low calibration frequency | 1~20
www.wps.cn 「 让PPT设计简单起来！」
15
Dunhuang
(40.138°N, 94.32°E)
Libya1
(24.42°N, 13.35°E)
Arab2
(20.13°N, 50.96°E)
DCC
Sea
DomeC
Moon
various targets

## Slide 16: SRB Validation Results From CRCS
On-orbit validation based on Integrated calibration (VC) and In situ CRCS using Dunhuang site
Prelaunch laboratory calibration perform well on-orbit, and the biases of most bands are within 5%. The two independent validation results show good consistency.
band | Center Spectral nm | Integrated-VC % | Dunhuang Insitu VC %
1 | 470 | -1.79 | -1.28
2 | 550 | 7.99 | 5.09
3 | 650 | 5.14 | 4.22
4 | 865 | 1.37 | 1.12
5 | 1380 | 14.63 | NaN
6 | 1640 | 2.47 | -2.6
7 | 2130 | 14.42 | 16.08
8 | 412 | -16.72 | -17.63
9 | 443 | -0.91 | -2.48
10 | 490 | 2.49 | -0.06
11 | 555 | 3.82 | 2.62
12 | 670 | -2.52 | -3.46
13 | 709 | 0.59 | -2.11
14 | 746 | 2.27 | 0.83
15 | 865 | 1.92 | 1.36
16 | 905 | 4.74 | NaN
17 | 936 | 7.22 | NaN
18 | 940 | 0.19 | NaN
19 | 1030 | -7.52 | -6.67
Validation results comparsion between integrated vicarious calibration (without insitu measurement) and Dunhuang site insitu calibration（2018.05）
Dunhuang VC
Integrated VC

## Slide 17: SRB Calibration Monitoring using Moon, DCC and Multi-sites
SRB bands degradation monitoring based on Moon、DCC、Multi-sites

## Slide 18: zz
412nm: ~3.3%
1030nm: ~2.5%
865nm: ~2.7%
555nm: ~2.7%
670nm: ~2.7%

## Slide 19: MERSI-II SRB Cal Bias After Correction
Bias <3% for most of MERSI-II SRB bands

## Slide 20: Land surface Reflectance vs MODIS within 5%
Validation Using MODIS LCD43 LSR

## Slide 21: Precipitation Water Vapor(PWV) from NIR using ground-based GPS

## Slide 22
AOD from MERSI-II for monitoring the haze activities

## Slide 23: HIRAS Cal/Val progress
Mar ,2018
- HIRAS infrared detectors powered on and Telemetry check
- Checks of 1st IGM, Raw Spectra, Calibrated spectra
- Initial alignment of Interferometer fixed-mirror
Apr, 2018
- Change of detector Temperature from 85Deg to 82Deg
- Fine alignment of Interferometer fixed-mirror
- Temperature cooling down of ICT
- Cold space observations
- ILS parameters tuning and NL coefficients generation
March ~ June commission test , 17 items
- NEdT evaluation, Spectral validation
- Radiance validation,Inter-pixel comparison
Aug, 2018
- commission finished
Dec, 2018
- Decontamination and turn on

## Slide 24: HIRAS Radiances from example SNO 32 spectra overlaid
Example of very uniform SNO shows good performance
From Hank Revercomb

## Slide 25: HIRAS compared to IASI-B single example SNO
Early SNO comparisons with IASI and CrIS are very promising
HIRAS
From Hank Revercomb

## Slide 26: HIRAS vs IASI
HIRAS
IASI
A first look to HIRAS data from EUMETSAT
Courtesy of Dorothee Team

## Slide 27: IASI/B vs. HIRAS (Antarctic)
A first look to HIRAS data from EUMETSAT
Courtesy of Dorothee Team

## Slide 28: HIRAS vs. IASI/B (Antarctic)
HIRAS
IASI
0,24K
All scenes
200000 IASI spectra
150000 HIRAS spectra
Difference HIRAS-IASIA - Antarctic
A first look to HIRAS data from EUMETSAT
Courtesy of Dorothee Team

## Slide 29: Spectral accuracy validation
HIRAS OBS compared with LBLRTM simulation in clear ocean condition.
Clear pixels filtering: Using MERSI cloud mask production.
Clear pixels determined from MERSI cloud mask
MERSI-II Cloudmask

## Slide 30
Spectral bias monitoring in 9 months, spectral bias is in range of 5ppm for MW and SW in 9 months. There is 5~10 ppm trend in LW, after on-orbit heating it recovered.
LW band
MW band
SW band

## Slide 31
HIRAS Evaluation with
GSICS LEO-LEO IR intercalibration
SNO collocation Method
Time Constrains: 10 minutes
Air Path Constrains
FOR 14-17 for CrIS
FOR 14-16 for HIRAS.
Distance constrains: 5 km
Scene uniformity
VIIRS and MERSI: std < 0.2K
Wang et al, 2016
Results with CrIS:
Data: 2018.04.25-2018.05.15 20 days
LW bias <0.5K，MW <0.7K；
LW bias std <0.3K，MW std 0.2~1K；

## Slide 32
Data:2018.04.22-2018.05.26 17 days
LW bt bias <0.5K，MW bt bias < 0.7K；
LW bias std <0.5K， MW bias std in 0.5~1K，
SW window and weak absorption region <0.5K, >0.5K @absorption ；

## Slide 33
4 months of HIRAS-CrIS bias monitoring shows stable error characteristics.
HIRAS-CrIS bias monitoring

## Slide 34
O-B monitoring shows stable bias
34
O-B using Chinese ARM radiative transfer model

## Slide 35
CH25
CH24
CH23
CH22
CH21
CH20
HIRAS
IR Band | MERSI |  |  | HIRAS(cm-1)
 | (Cm-1) | (μm) | IFOV(m) | 
CH25 | 833.33 | 12.0 | 250 | 650-1135 (LW)
CH24 | 925.93 | 10.8 | 250 | 
CH23 | 1169.59 | 8.55 | 1000 | 
CH22 | 1388.89 | 7.2 | 1000 | 1210-1750 (MW)
CH21 | 2469.14 | 4.05 | 1000 | 2155-2550 (SW)
CH20 | 2631.58 | 3.8 | 1000 | 
4 bands are fully covered by HIRAS, 2 LW 1 MW, 1 SW;
2 bands in spectral gap;
Inter-Comparison between HIRAS vs MERSI-II
Notes: 加阴影

## Slide 36
An accurate collocation method from GSICS is used for inter-calibration on the same platform. (Wang et al., 2013,2016).
Satellite
P
Accurate collocation Method
Computing the two sensor’s pointing vector;
Comparing the angle between pointing vectors with HIRAS’s FOV size angle;
Finding exactly which MERSI pixels are in HIRAS’s FOV.
Accurate collocation is based on line-of-sight pointing vectors, but not the spatial location.

## Slide 37
Before and After scene uniformity check
MERSI-HIRAS bias changed with scene brightness temperature
Collocated Samples filtering of MERSI-HIRAS

## Slide 38
HIRAS Geolocation Evaluation
MERSI
MERSI-HIRAS
Local Zoom-in
Radiation of the two instruments shows a significant difference in the inhomogeneous targets, especially at coastline;
Bias has no systematic error along the coastline;
Geolocation inconsistency was found at the beginning of commissioning.
Notes: The radiation of MERSI and HIRAS shows a significant difference in the inhomogeneous targets, especially at coastline, that means the geolocations of MERSI and HIRAS are inconsistency. If we enlarge the coast line area, we found the bias has no systematic error along the coastline. The bias distribution of traditional geolocation inconsistency will show that, on one side of the coastline the bias are positive and on the other side, the bias are negative. But here is not. So the geolocation inconsistency between MERSI and HIRAS are not the traditional kind.

## Slide 39
FOV4
FOV2
FOV3
FOV1
 | X | Y
FOV1 | -37 | 3
FOV2 | 32 | 0
FOV3 | 31 | 2
FOV4 | -32 | 3
The FOVs maybe reverse left and right!
Low latitude, nonuniformity samples
FOR 13-17，near nadir samples
Geolocation consistency
Orbit Direction
Scan Direction
Checking geolocation consistency between 4 FOVs
Notes: In order to analysis this phenomenon, we need to check geolocation consistency between 4 FOVs. We check the correlation of each HIRAS FOV image and the collocated MERSI’s image. The method is, we shift the MERSI image along the scan and along the orbit direction， and after each step, we can get a RMSE. The location of minimum of RMSE coincide the geolocation inconsistency between HIRAS and MERSI.
Here we choose the near nadir low latitude and nonuniformity samples to do this work. We can see from this result that, the minimum RSME of FOV1 is negative 37 along the scan, and the FOV3 is 32. It means that the FOV maybe reverse left and right

## Slide 40
Results after geolocation correction
HIRAS
MERSI
MERSI-HIRAS
before
after

## Slide 41
 | CH21 (SW) | CH22 (MW) | CH24 (LW) | CH25 (LW)
FOV1 | -0.160±0.170 | 0.096±0.177 | -0.402±0.253 | -0.252±0.192
FOV2 | -0.165±0.177 | 0.182±0.186 | -0.399±0.149 | -0.346±0.170
FOV3 | -0.186±0.319 | 0.389±0.312 | -0.420±0.279 | -0.258±0.236
FOV4 | -0.167±0.169 | 0.242±0.251 | -0.422±0.327 | -0.256±0.247
In MW, the FOV3’s bias is much higher than the others, the difference between FOV3 and the minimum bias is nearly to 0.3 K;
In SW and LW, the biases between MERSI and HIRAS in 4 FOVs are similar to each other;
FOV3
7.2μm bias at different BT
Non-linear feature of 4 FOVs are difference;
FOV3’s non-linearity seems more significant than others;
Bias analysis: stripe
FOVs radiometric consistency
Notes: The further work is still ongoing

## Slide 42
LW
MW
SW
HIRAS bias in different FOVs
FOV3’s bias has a little departure from other FOVs

## Slide 43
The bias at 7.2μm is increase with scan angle;
Bias at nadir is minimum, and the maximum appears at edge of scan;
All FOVs’ bias increase with scan angle;
Bias analysis: angle dependent bias
Results: Bias Angle dependence

## Slide 44
Iner-Comparison between
MERSI-II and HIRAS
collaboration of intercalibration in the different and same platform.
Before correction
After correction
TEBs OBC paremeters correction use IASI and CrIS as reference
Notes: IASI and CrIS is used as reference for MERSI II TEBs OBC paremeters correction, and MERSI and HIRAS inter-calibration can be used for global validation based on GSICS Fine Collocation method of Sounder with Imager

## Slide 45
Before correction
After correction

## Slide 46: Contamination Issue
Gas emission and condensation from inside instrument glues
Daily monitoring of ISRF degrading as compared with 2018.04.21.

## Slide 47: Signal Response and NEDT Degradation
Daily monitoring of ISRF degrading at typical spectral absorbing positions (LWIR: 801.2cm-1, MWIR: 1259.29cm-1, SWIR:2339.2cm-1).
NEdT after HIRAS 8-months operation (2018.12.20).
NEdT after HIRAS post-launch Cal/Val test (2018.04.25).

## Slide 48: MERSI-II/HIRAS Cal/Val Continuity
GSICS SNO or SNOx monitoring using reference instruments (IASI, CrIS, MODIS,VIIRS) and Intercomparison with EUMETSAT partner sensors including Sentinel 3 OLCI/+SLSTR, GOME-2.
Operational Instrument Performance Monitoring for long term based on OBC complete telemetry parameters
MERSI-II Calibration trend monitoring will be kept going using PICS sites, DCC, moon and ground-based automatic measurements at Dunhuang site. Integrated calibration system will be established which combines earth targets, moon, DCC and RT simulation.
The improvement of HIRAS nonlinear correction and polarization upgrade are kept on going.
HIRAS contamination is kept on monitoring and Its decontamination will be done every six months.

## Slide 49
Band | Spectral Range (cm-1) | Spectral Resolution (cm-1) | Sensitivity (NET@280K) |  |  | Num of Channels
 |  |  | FY-3D | FY-3E |  | 
LWIR | 650～1136 （15.38m～8.8 m） | 0.625 | 0.15(Expectation) 0.4K(Requirement) | 650 ～667 cm-1 | 0.8K | 778
 |  |  |  | 667～689 cm-1 | 0.4K | 
 |  |  |  | 689～1000 cm-1 | 0.2K | 
 |  |  |  | 1000～1136 cm-1 | 0.4K | 
MWIR1 | 1210～1750 （8.26m～5.71 m） | 1.25 | 0.1(Expectation) 0.7K(Requirement) | 1210～1538 cm-1 | 0.2K | 433
 |  |  |  | 1538～1750 cm-1 | 0.3K | 
MWIR2 | 2155～2550 （4.64m～3.92 m） | 2.5 | 0.3(Expectation) 1.2K(Requirement) | 2155～2300 cm-1 | 0.3 | 159
 |  |  |  | 2300～2550 cm-1 | 0.5 | 
HIRAS Improvement from FY-3D to FY-3E Early Morning orbit
FY-3D
FY-3E
designed & built at Shanghai Institute of Technical Physics

## Slide 50: Global Image Mosaic of MERSI-II Clear Sky images
Courtesy of Yanting Wang

## Slide 51: Global Image Mosaic of MERSI-II Clear Sky images
D星看美丽星球
Courtesy of Yanting Wang

## Slide 52
美丽星球
Global Image Mosaic of MERSI-II Clear Sky images
Courtesy of Yanting Wang

## Slide 53
风云三号晴空数据集效果展示
North American Image Mosaic of MERSI-II Clear Sky images
Courtesy of Yanting Wang

## Slide 54: Email：huxq@cma.cn Tel: 68407463 Cell phone: 17710267179 National Satellite Meteorological Center, CMA
Thanks！