## Slide 1
Lei Yang1, Peng Zhang1, Zhongdong Yang1, Songyan Gu1, Aijun Zhu1, Xiuqing Hu1, Di Xian1, Xiuzhen han1, Maonong Ran2, Ping Qin2 and Xuexing Guo2
1: National Satellite Meteorological Center ,CMA
2: HuaYun ShineTek.
yangl@cma.gov.cn
June 2019, IMAPP/CSPP 2019 , Chengdu, China
Evolution of Fengyun-3
Direct Broadcasting Software Package

## Slide 2
Outline
Brief history and future for Fengyun-3
Typical Receive equipment and software
FY-3 HRPT/MPT status
DB User distribution
Typical Applications

## Slide 3
Satellite | Launch | Nature | Design life | Status
FY-3A | May 27, 2008 | Experimental | 3 years | Retired
FY-3B | Nov. 5, 2010 | Experimental | 3 years | Operational
FY-3C | Sep. 23, 2013 | Operational | 5 years | Operational
FY-3D | Nov. 15, 2017 | Operational | 5 years | Operational
FengYun Polar-orbiting meteorological satellites
1. Brief of FengYun Polar satellites
FY-3A/C：AM Orbit
FY-3B/D: PM Orbit
FY-3C(AM)
FY-3D(PM)
FY-3B(PM)
FY-3A(AM)

## Slide 4: Future Plan for Fengyun Polar-orbiting series
Polar-orbiting series | Satellite | Orbit | Launch | Design life
The 3rd batch of FY-3 | FY-3E | Early morning | 2020(plan) | 8 years
 | FY-3F | AM | 2021(plan) | 8 years
 | FY-3G | Inclined orbit | 2022(plan) | 6 years
 | FY-3H | PM | 2023(plan) | 8 years
The 4th batch of FY-3 | FY-3I | Early morning/AM | 2025(plan) | 8 years
 | FY-3J | Inclined orbit | 2027(plan) | 7 years
Satellite | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035
FY-3E |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
FY-3F |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
FY-3G |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
FY-3H |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
FY-3I |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
FY-3J |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
EM
AM
RM
PM

## Slide 5: Future Fengyun Satellite Fleet
In the next 10 years, CMA will have 6 LEO operational satellites.
The LEO realizes the network of covering the EM, AM and PM satellite observation, and the time limit of global data updating has been raised from 6 hours to 3 hours. Fine detection of elements such as precipitation and greenhouse gas.
FY-3E(EM)
FY-3 (09/10)
FY-3F(AM)
FY-3G(PM)
FY-3R(Inclined)
Orbit 1(for EM,AM,PM)
  type：sun synchronous orbit
  Orbit altitude：836km
  Orbit inclination：98.7°
Orbit 2(for RM)
  type：Low inclination orbit
  Orbit altitude：407km
  Orbit inclination：50°

## Slide 6
Payloads & Measurement Capability of LEO Programme
Item | Sensor Suite | Satellite Sensor | FY-3A (AM) | FY-3B (PM) | FY-3C (AM) | FY-3D (PM) | FY-3E EM | FY-3F AM | FY-3G PM | FY-3R Rainfall
1 | Optical Imagers | MERSI | √ | √ |  |  | √（LL） | √（III） | √（III） | √（III-Simplified）
2 | Passive Microwave Sensors | MWTS | √ | √ |  |  | √ | √ | √ | 
 |  | MWHS | √ | √ |  |  | √ | √ | √ | 
 |  | MWRI | √ | √ |  |  |  | √ | √ | √
3 | Occultation Sounder | GNOS |  |  |  |  | √ | √ | √ | √
4 | Active Microwave Sensors | WindRAD |  |  |  |  | √ | √ |  | 
 |  | Rainfall RAD |  |  |  |  |  |  |  | √
5 | Hyperspectral Sounding Sensors | HIRAS |  |  |  |  | √ | √ | √ | 
 |  | GAS (Greenhouse Gases Absorption Spectrometer) |  |  |  |  |  |  | √ | 
 |  | OMS (Ozone Mapping Spectrometer) |  |  |  |  |  | √ |  | 
6 | Radiance Observation Sensor Suite | ERM | √ | √ |  |  |  | √ |  | 
 |  | SIM | √ | √ |  |  | √ | √ |  | 
 |  | SSIM (Solar Spectral Irradiation Monitor) |  |  |  |  | √ |  |  | 
7 | Space Weather Sensor Suite | SEM | √ | √ |  |  | √ |  |  | 
 |  | Wide Angle Aurora Imager |  |  |  |  |  |  | √ | 
 |  | Ionosphere photometer |  |  |  |  | √(Multi-angle) |  | √ | 
 |  | Solar X-EUV Imager |  |  |  |  | √ |  |  | 

## Slide 7
FY-3C sounding data have been assimilated into CMA GRAPES, ECMWF, UK NWP model operationally.
Kangerlussuaq
Svalbard
Athens
Lannion
Maspalomas
EUMETSAT Advanced Retransmission Service
Global Data
Regional Data
International User Community

## Slide 8
Cost Function
The data quality is now comparable to that from equivalent US and European meteorological satellites

## Slide 9
Important Component of WMO Space Program
  reliable and sustained observation in operation
  open data policy to free access

## Slide 10: Typical Receiving Equipment
Antenna key parameters: | 
Diameter | 4.2m
Frequency | L band 1698 ~1710 MHz X band7750 ~ 7850 MHz 8025~8400MHz
Gain | L band- GLR33.3＋20log(f/1.698)dBi X band- GXR46.9＋20log(f/7.75)dBi
Modulation | BPSK/QPSK

## Slide 11: DB Software Features
For DB data preprocessing
FY-3 preprocessing software package is a software system for preprocessing direct broadcast (DB) data from FY-3 series satellites.
It supports processing DB data of VIRR, MERSI, MWHS, MWTS, IRAS/HIRAS and MWRI from FY-3A, FY-3B , FY-3C, FY-3D.
It consists of two software packages, FY-3 MPT/HRPT Level-0 data generation software package and FY-3 MPT/HRPT Level-1 data preprocessing software package.
Testing data will provided via the software package in the future.
Both the software and satellite to ground interface document can be abtained via http://satellite.nsmc.org.cn.
For FY-3D,
  Software development group has been set up since May 2017,
  FY-3D launch date, Nov 2017. Operational software allocated in NSMC started to work. The first version for DB software has been set up since then.
  In April 2018, the DB software has been modified and updated according to the on-orbit test results.
  The software has been delivered to inner quality management for software test and the test was finished in July 2018.
  The first version for DB SW has been delivered to the public on 27 Aug. 2018.
  An updated version has been provided according to the users feedbacks in April 2019.
Notes: New feature:提供测试数据，提供多线程处理，等等新特性

## Slide 12: User Guide

## Slide 13: Environment for operating DB oftware
Operating system: CentOS_6.3_x64 Linux
Recommended hardware configurations are as follows:
  RAM: >4.0GB
  CPU: Intel Pentium multi-core processor (>3.0Ghz)
Hard disk: >200GB

## Slide 14
FY-3 HRPT/MPT Status
Extended Spatial Coverage after FY-3C satellite power shortage
FY-3B: HRPT + MPT, MPT(MERSI), HRPT(other data except MERSI), suffering from power shortage, FY-3B HRPT/MPT only covers China and Europe.
FY-3C: Only HRPT can work due to the power problem. It only covers China and Europe.
FY-3D: FY-3D and follow-ons use X-band MPT channel.

## Slide 15: User Distribution
More than 45 International DB Users across 24 countries. At least 116 users who get VASS data by the service EARS-VASS(Eumetsat Advanced Retransmission Service).
Notes: EARS的用户分布

## Slide 16: User Distribution
More than 60 DB Users inside China.
Notes: EARS的用户分布

## Slide 17: Typical Applications by using DB Data
With those efforts, NSMC try to help advancing the NWP, climate and environmental communities.
Monitoring of cyanobacteria bloom
图1 FY-3D气象卫星太湖蓝藻水华监测图 ( 2018年5月8日)
图2 FY-3D气象卫星太湖蓝藻水华强度示意图 ( 2018年5月8日)
Figure1 Cyanobacteria bloom monitoring（May 8 2018）

## Slide 18
图2 FY-3D气象卫星黄海海域浒苔监测示意图 ( 2018年6月1日)
图1 FY-3D气象卫星黄海海域浒苔专题图 ( 2018年6月1日)
Algae monitoring
Typical Applications by using DB Data
Figure1 Algae monitoring（June 1 2018）

## Slide 19
urban heat island Monitoring
Typical Applications by using DB Data
Figure1 Urban heat island monitoring（June 20 2018）

## Slide 20
Fire
图2 FY-3D气象卫星内蒙古自治区呼伦贝尔市火情监测图
（2018年6月2日12时15分）
Snow
图1 FY-3D气象卫星东北区域积雪专题图（2018年3月15日12时）
Typical Applications by using DB Data
Figure1 Fire monitoring（June 2 2018）

## Slide 21
Sea-ice
图1 FY-3D气象卫星渤海湾海冰监测专题图
（2018年1月31日13时）
图2 FY-3D气象卫星渤海湾海冰监测图
（2018年1月31日13时）
Typical Applications by using DB Data
Figure1 Sea ice monitoring（31 Jan 2018）

## Slide 22
volcanic ash cloud
Fig.1 Guatemala volcanic ash cloud
（4 June 2018 02:55 Beijing Time）
Typical Applications by using DB Data

## Slide 23
Sand storm
）
Typical Applications by using DB Data
Figure1 Sand storm monitoring（May 8 2018 UTC1500）

## Slide 24
Fog
Typical Applications by using DB Data
Figure1 Fog monitoring（26 March 2018）

## Slide 25
Global monitoring
Typical Applications by using DB Data

## Slide 26
Thank you for your attention!
Lei Yang
National Satellite Meteorological Center, CMA
yangl@cma.gov.cn